## Slide 1: WF on LAA DL LBT ED Threshold Adaptation Rule (Functionality of Detecting On-going 802.11 a/n/ac tx)
Cisco Systems, Broadcom, CableLabs, Ruckus Wireless
3GPP TSG RAN WG1 #83 R1-157626
Anaheim, USA
15th – 22nd November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Proposal
For the functionality when an LAA eNB is capable of detecting and attempts to detect, for LBT, the presence (including start and duration) of 802.11a/n/ac transmission on the same channel that the LAA eNB intends to transmit on, then
  Detection Threshold for detecting the presence (including start and duration) of 802.11 a/n/ac transmission = -82 dBm in the absence of interference
  Maximum single channel ED threshold = Tmax
    Tmax = -75 dBm/MHz + 10*log10(BW) (MHz)
  Upon detecting presence of an ongoing 802.11a/n/ac transmission (including start and duration), the LAA eNB should regard the channel as busy for the purpose of Cat-4 LBT for the duration of the 802.11a/n/ac transmission

## Slide 3: Proposal
If the LAA eNB is aware of the absence of co-channel 802.11 BSS (e.g. via regulation or via planning)
  Maximum single channel ED threshold = Tmax