## Slide 1: WF on RAR for MTC
Ericsson, NTT DoCoMo, Qualcomm, Sony
3GPP TSG RAN WG1 Meeting #83 R1-157725
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Background
Agreement:
For a given PRACH coverage enhancement level, the corresponding M-PDCCH search space scheduling RAR for the UE to monitor is derived at least based on MTC-SIB
MTC-SIB explicitly indicates the following information for M-PDCCH scheduling RAR:
  The set of numbers of repetitions or the max number of repetition (while other numbers of repetition are implicitly derived)
    To be concluded offline which one to use
  Other information related to M-PDCCH is FFS – Wang Yi (HW)
The starting subframe(s) of the search space for the M-PDCCH scheduling RAR is explicitly indicated in MTC-SIB
  The same configuration of the starting subframe(s) also applies to the case of message 3 re-transmissions and message 4
    FFS when C-RNTI is already configured for a UE
  FFS the details of the signalling – Yunjung (LGE)

## Slide 3: Proposals on CSS configuration for RAR
One or more narrowbands are explicitly indicated in MTC-SIB for M-PDCCH for RAR for each PRACH repetition level
  No need to indicate PRB resource location within each narrowband
When more than one narrowband is configured for M-PDCCH for RAR for a PRACH repetition level,
  The narrowband is selected based on the PRACH preamble index (implicit mapping)