## Slide 1: WF on Frequency Hopping Configurations
Nokia Networks, Ericsson, ALU, ASB, InterDigital, Intel, Sony, CATT, Panasonic, Sierra Wireless, MediaTek, Samsung, NEC, DoCoMo, Qualcomm, LGE, ZTE
R1-157761
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.2

## Slide 2: Proposal
Frequency hopping configuration for M-PDCCH, select one option –
  Option 1:
    CSS/Msg4: The first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset
      FFS whether the offset is UE-specific or cell-specific
    USS: The narrowbands used are explicitly signaled to the UE
  Option 2:
    The first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset
      FFS whether the offset is UE-specific or cell-specific

## Slide 3: Proposal
Frequency hopping configuration for PDSCH –
  The first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset
    FFS whether the offset is UE-specific or cell-specific
In CE Mode A, on/off of unicast PDSCH frequency hopping is dynamically indicated by DCI if PDSCH hopping is enabled by higher-layer signaling

## Slide 4: Proposal
Frequency hopping configuration for PUSCH –
  PUSCH BW within the system BW for frequency hopping is configured
    NOTE: Motivation is to avoid collision with PUCCH (similar to Rel-8 pusch-HoppingOffset parameter)
  The first narrowband is signaled, the other narrowband is determined using a configurable offset
    FFS whether the offset is UE-specific or cell-specific
In CE Mode A, on/off of PUSCH frequency hopping is dynamically indicated by DCI if PUSCH hopping is enabled by higher-layer signalling

## Slide 5: Proposal
PRACH frequency hopping is between two frequencies
Frequency hopping configuration for PRACH –
  prach-FreqOffset is signaled, the other frequency for PRACH is determined using a configurable offset

## Slide 6: Proposal
Narrowbands for PUCCH frequency hopping are symmetric to the central frequency of system bandwidth