## Slide 1: WF on Remaining Configurations regarding Starting Subframe Set Configuration
LG Electronics, ...
R1-157769
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.10

## Slide 2: Background
The starting subframe(s) of the search space for the M-PDCCH scheduling RAR is explicitly indicated in MTC-SIB
  The same configuration of the starting subframe(s) also applies to the case of message 3 re-transmissions and message 4
    FFS when C-RNTI is already configured for a UE
  RAN1 recommends to have [3] bit for the signalling, and kindly ask RAN2 to specify the details of the signalling

## Slide 3: Proposal for USS
For starting subframe for USS, decide between
  Option 1. Separate RRC parameter:
    RAN1 recommends to have [3] bit for the signalling, and kindly ask RAN2 to specify the details of the signalling
  Option 2. No new RRC parameter:
    reuse [3] bits configured for the starting subframe to the M-PDCCH scheduling RAR is explicitly indicated in MTC-SIB

## Slide 4: Proposal for PRACH
To support TDM among different CE levels, per each CE level, the following can be configured
  3-bit Periodicity P for PRACH repetition level R
    E.g., {Rmax/8, Rmax/4, Rmax/2, Rmax, Rmax *2, reserved} where Rmax = 128
  2-bit Offset
    {0, P/8, P/4, P/2}
  If the parameter is not given, a UE assume starting subframe of PRACH is determined implicitly based on
    PRCH repetition level R, PRACH resource configuration index and SFN/subframe index