## Slide 1: WF on Remaining details on RPF=4 SRS
Qualcomm, ZTE, CMCC
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th-22nd November 2015
Agenda Item: 6.2.4.2.2
R1-157786

## Slide 2: Background
In RAN1 meeting #82bis, the following conclusions have been reached regarding SRS capacity improvement for EBF/FD-MIMO:
Agreement:
A new RRC parameter is introduced for a Rel-13 UE to determine the length of additional UpPTS symbols.
  The number of additional UpPTS symbols is indicated to the UE with the RRC parameter with two states – {2, 4}.
  Note: The number of total UpPTS SC-FDMA symbols does not exceed 6 in a special subframe
  Note: The number of DwPTS symbols is the same as the number of DwPTS symbols in the legacy special subframe configuration in SIB1.
  For trigger types 0 and 1, a new set of RRC parameter values for additional UpPTS are separately configured from the legacy SRS configurations, where the parameters are the same as the ones used for legacy SRS.
Agreement:
Confirm the working assumption to increase number of combs to 4 with maximum number of CS=12
  A new RRC signalling is introduced to enable RPF4
  The UE-specific parameter transmissionComb or transmissionComb-ap is extended to two bits to indicate 4 indexes of comb.
  One additional signalling bit is added to indicate 12 cyclic shifts together with the existing 3 bits

## Slide 3: Background
For the existing RPF=2 SRS with 4-ports, the cyclic shift and transmission comb per port are defined by
 | CS ( ) |  |  |  | comb |  |  | 
0 | 0 | 2 | 4 | 6 | transmissionComb | transmissionComb | transmissionComb | transmissionComb
1 | 1 | 3 | 5 | 7 | transmissionComb | transmissionComb | transmissionComb | transmissionComb
2 | 2 | 4 | 6 | 0 | transmissionComb | transmissionComb | transmissionComb | transmissionComb
3 | 3 | 5 | 7 | 1 | transmissionComb | transmissionComb | transmissionComb | transmissionComb
4 | 4 | 6 | 0 | 2 | transmissionComb | 1-transmissionComb | transmissionComb | 1-transmissionComb
5 | 5 | 7 | 1 | 3 | transmissionComb | 1-transmissionComb | transmissionComb | 1-transmissionComb
6 | 6 | 0 | 2 | 4 | transmissionComb | 1-transmissionComb | transmissionComb | 1-transmissionComb
7 | 7 | 1 | 3 | 5 | transmissionComb | 1-transmissionComb | transmissionComb | 1-transmissionComb

## Slide 4: Proposal
For RPF=4 SRS configuration,
  the length of the sequence is defined as
  the cyclic shift is given by
  where =0…-1 and ={0…11} is configured CS value

## Slide 5: Proposal
FFS on whether and how to apply RPF=4 for 4 port SRS case:
  The transmission comb per port of the RPF=4 SRS is given by
  Example 1
  Example 2
  Example 3

## Slide 6: Proposal
For SRS transmission in extended UpPTS, the determination of frequency domain starting position is same as legacy UpPTS