## Slide 1: WF on RAR reception and Msg3/Msg4 scheduling
Huawei, HiSilicon, …
3GPP TSG RAN WG1 Meeting #83 157825
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.1

## Slide 2: Proposals for RAR
For LC/CE UEs in RRC_IDLE state, if the reception of RAR collides with the reception of an updated MTC-SIB, the updated MTC-SIB is prioritized.
For LC/CE UEs in RRC_CONNECTED state, if the reception of RAR collides with an unicast DL transmission, the RAR is prioritized.

## Slide 3: Proposals for Msg3/Mg4
Agree that
the narrowband index of M-PDCCH for Msg3 re-transmission or Msg4 transmission is determined by
  Alt 1: implicitly derived by the preamble index of the last successful PRACH attempt