## Slide 1: WF on UL grant in RAR
Lenovo, Ericsson, Samsung
R1-157860
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.7

## Slide 2: Proposal
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
Msg3 narrowband index | ceil(log2(number of narrowbands)) | 2 | NB index of Msg3 scheduling
PRB assignment | 4 | 3 | PRB location within the configured narrowband in narrowband index field.
Repetition number | 2 | 3 | The repetition level of Msg 3 is dynamically indicated based on a set of values configured by higher layers.
MCS | 3 | 2 | MCS/TBS
TPC | 3 | 0 | TPC is supported in CE mode A
A-CSI | 1 | 0 | A-CSI is supported in CE mode A
UL delay | 1 | 0 | 
Msg3/4 M-PDCCH narrow band index | 2 | 2 | NB index of M-PDCCH carrying Msg3 ReTx and Msg4
Total | 20 | 12 | 

## Slide 3: Proposal
Msg3 narrowband index in Mode B
    NB_RAR = narrowband used for first subframe of M-PDCCH for RAR
    NB_Msg3 = narrowband used for first subframe of Msg3 PUSCH transmission
    N_NB = the total number of UL narrowbands in the system bandwidth
    Bits=00  NB_Msg34 = (NB_RAR + 0) mod N_NB
    Bits=01  NB_Msg34 = (NB_RAR + 1) mod N_NB
    Bits=10  NB_Msg34 = (NB_RAR + 2) mod N_NB
    Bits=11  NB_Msg34 = (NB_RAR + 3) mod N_NB

## Slide 4: Proposal
Msg3/4 M-PDCCH narrowband index in Mode A and Mode B
    NB_RAR = narrowband used for first subframe of M-PDCCH for RAR
    NB_Msg34 = narrowband used for first subframe of M-PDCCH for Msg3 retransmission and first subframe of M-PDCCH for Msg4
    N_NB = the total number of DL narrowbands in the system bandwidth
    Bits=00  NB_Msg34 = (NB_RAR + 0) mod N_NB
    Bits=01  NB_Msg34 = (NB_RAR + 1) mod N_NB
    Bits=10  NB_Msg34 = (NB_RAR + 2) mod N_NB
    Bits=11  NB_Msg34 = (NB_RAR + 3) mod N_NB