## Slide 1: WF on PRACH frequency retuning gap for MTC
Ericsson
R1-157863
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.2

## Slide 2: Proposal
When the UE retunes between a first PRACH narrowband in one subframe and a second PRACH narrowband in the next subframe, the retuning gap is assume to correspond to maximum 2 DL OFDM symbols.
A guard time can be arranged by the UE by truncating the transmission in
  Option α: the beginning of the later PRACH subframe
  Option β: the guard time already available in the earlier subframe plus the beginning of the next PRACH subframe
  Option γ: up to the UE implementation