## Slide 1: WF on remaining details on SPS
Qualcomm, Nokia, Intel, Samsung
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.11

## Slide 2: Proposal: grant validation for activation
The following fields are reserved for the activation DCI
  M1A:
    TPC for PUCCH: used to select PUCCH configuration from the 4 configured in RRC
    HARQ process number
    RV
  M0A:
    TPC command for scheduled PUSCH.
    Cyclic shift DMRS
    HARQ process number
  The repetition number is derived from DCI following the same mechanism as dynamic PDSCH/PUSCH.

## Slide 3: Proposal: grant validation for deactivation
The following fields are reserved for the deactivation DCI
  M1A:
    Field(s) used for resource allocation
    HARQ process number
    MCS
    RV
    Repetition number
  M0A:
    Field(s) used for resource allocation
    MCS and RV
    TPC command for scheduled PUSCH
    DMRS Cyclic shift
    Repetition number

## Slide 4: Proposals on prioritization
Dynamically scheduled PDSCH and PUSCH have higher priority than semi-persistent scheduled PDSCH and PUSCH
For collisions between semi-persistent scheduled PDSCH and PUSCH and other channels, same rules as dynamically scheduled PDSCH and PUSCH apply.