## Slide 1: WF on Collision Handling for MTC
Ericsson, Panasonic, Samsung
R1-157885
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.5

## Slide 2: Proposal: Downlink
When in RRC_CONNECTED, MPDCCH scheduling RAR and PDSCH conveying RAR that are related to M-PDCCH order is prioritized over any other unicast DL reception
If scheduled PDSCH reception and M-PDCCH monitoring opportunity fully or partially overlap in time and are located at different narrowbands, scheduled PDSCH reception is prioritized over M-PDCCH monitoring opportunity
  Note: If scheduled PDSCH reception and M-PDCCH monitoring opportunity are located at the same narrowbands, UE performs both functions:
    Receives the scheduled PDSCH
    Monitors M-PDCCH candidates in resources not occupied by the PDSCH

## Slide 3: Proposal: CSI-RS
UE assumes that M-PDCCH/PDSCH REs occupied by CSI-RS are punctured