## Slide 1: WF on details of PUCCH design for MTC
Ericsson, Panasonic
R1-157886
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.6

## Slide 2: Proposal: PUCCH resource determination
For PUCCH resource determination, nECCE numbering is following:
  When 24 eCCEs are detected by UE, it uses nECCE = 0 of 4 PRB-set.

## Slide 3: Proposal: ACK/NACK bundling
Mapping of ACK/NACK bits and PDSCH subframe is according to:
  One ACK/NACK bit is generated corrresponding to subframe index of the last subframe carrying the PDSCH
  The ACK/NACK bit is used in bundling/multiplexing of PUCCH