## Slide 1: WF for UE capabilities and category
MediaTek, InterDigital, Intel, CATT, Panasonic, Ericsson, Sony, Spreadtrum,…
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda Item: 6.2.1.1
R1-157888

## Slide 2: Proposals for UE behavior and capability in HD-FDD
Proposal 1: For HD-FDD, type B operation is assumed.
Proposal 2: For HD-FDD, Similar to legacy behaviour, UE is expected to monitor DL transmission (e.g., M-PDCCH monitoring) unless explicitly signalled to perform UL transmission. When the UE is requested to perform UL transmission, the UL transmission is prioritized over DL reception.

## Slide 3: Proposal for UE capability
Proposal 1: for Rel13 eMTC UE, CE mode A is mandatory and CE mode B is optional. For the non-eMTC UE, CE mode B is optional.

## Slide 4: Proposals for UE category (1/2)
Proposal 1: Total number of soft channel bits is [25344] for Rel13 eMTC UE.

## Slide 5: Proposals for UE category (2/2)
Proposal 2: Define a new UE DL category (e.g., DL Category M1) based on only 1.4MHz bandwidth support and non-simultaneous reception of TBs
Proposal 3: Define a new UE UL category (e.g., UL Category M1) based on only 1.4Mhz bandwidth support
Proposal 4: Define a new combination of DL category M1 and UL category M1 for indication of total L2 buffer size.
Proposal 5: No indication of UE category for a combination of DL category M1 and UL category M1.