## Slide 1: WF on HD-FDD for NB-IoT
Sony, Nokia, ALU, ASB, Panasonic, Virtuosys, Ericsson, Intel, MediaTek, ZTE, Sierra Wireless, Interdigital, Qualcomm
R1-161124
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.1.2

## Slide 2: Background
The NB-IoT WID states that the NB-IoT UE will operate according to HD-FDD principles:
“An NB-IoT UE only needs to support half duplex operations”

## Slide 3: Proposals
On HD-FDD NB-IoT
  The guard period uses Type B HD-FDD guard period
    Timing relationship between NB-PDCCH and NB-PUSCH need to take this into account
  When NB-IoT UE is transmitting, UE is not expected to monitor or receive any downlink channels