## Slide 1: WF on Channel Modeling Methodology
Samsung
3GPP TSG-RAN WG1 #84
St. Julian’s, Malta, February 15 – 19, 2016
Agenda item: 7.3.5
Document for : Decision
R1-161150

## Slide 2: Proposal
The channel model in this SI should be based on the stochastic modeling methodology that is used for the 3D spatial channel model of TR 36.873, but with additional features >6GHz in the next page to fulfill the agreed requirements in R1-161142 and the agreed scenarios in R1-161145.
The behavior of the channel model in this SI for frequencies below 6 GHz should be fully consistent with that of the 3D spatial channel model of TR 36.873, if the additional features are not applied.
Consistent extension of the additional features to <6GHz can be considered after those features have been specified for >6GHz
  The extensions should not significantly impact simulation results already produced for below 6 GHz
  The extensions should not significantly increase simulation complexity.

## Slide 3: Proposal
The following additional features should be included in the channel model considered in the SI. FFS how to model these additional features, e.g., one modeling component may be able to satisfy multiple features.
  Foliage, atmosphere and rain attenuations as a function of frequency
  The blockage caused by the static objects and moving objects such as human body and vehicle: The blockage attenuation generally increases with frequency
  The spatial consistency which involves the evolutionary features and the correlation of channels between adjacent UEs or links on the large and small scale. This is useful for support of massive MIMO, mobility and beam trackings
  Support of large bandwidth (possibly up to 10% of carrier frequency)
  Support of 3D beamforming with large arrays
Additional features and modifications to a specific methodology should be introduced only when needed to address additional 5G modelling requirements and scenarios that will be agreed upon within the present Study Item.
Proponent Companies of additional features are encouraged to bring more Investigation of detailed modelling including map based or hybrid or stochastic methodologies for some scenarios, e.g., open square, indoor, is recommended. along with evidence showing the importance.