## Slide 1: Way Forward on joint reports of CRI for periodic CSI
ZTE, LGE, Samsung
R1-161210
Agenda Item: 7.1.4
Document for: Discussion and Decision
3GPP TSG-RAN WG1#84
St Julian’s, Malta, 15th - 19th February 2016

## Slide 2: Background
In RAN1#83, the following agreements have been reached.
When CRI and RI (of the same CC/CSI-process/subframe subset) are in the same subframe (i.e., when CRI offset = 0),
  The bitwidth of RI is determined using the same mechanism as in Rel-12, with the following exception
    For a given CSI process, if the number of antenna ports is used to determine RI width, the number of antenna port is replaced by using the maximum of Nk of the CSI process configured for the UE
  The bitwidth of W1/PTI is determined using the same mechanism as in Rel-12, with the following exception
    For a given CSI process, if the number of antenna ports is used to determine W1/PTI width, the number of antenna port is replaced by using the maximum of Nk of the CSI process configured for the UE

## Slide 3: Proposal
When K>1 and at least one of the configured CSI-RS resources has 8 CSI-RS ports or 4 CSI-RS ports with alternativeCodeBookEnabledFor4TX-r12=TRUE
and at least one of the configured CSI-RS resources has 1 or 2 CSI-RS ports or 4 CSI-RS ports without alternativeCodeBookEnabledFor4TX-r12 configured,
W1 or PTI in the joint report with CRI is set to zero if the selected CSI-RS has 1 or 2 CSI-RS ports or 4 CSI-RS ports without alternativeCodeBookEnabledFor4TX-r12 configured.