## Slide 1: WF on timing between NB-PDCCH NB-PDSCH and NB-PUSCH
ZTE, Sharp, …
R1-161258
3GPP TSG RAN WG1 #84 meeting
St. Julian, Malta, 15th – 19th February 2016
Agenda item 7.2.1.1.2

## Slide 2: Proposals
UE assumes that the timing offset between the ending subframe of NB-PDCCH and starting subframe of NB-PDSCH are in the same scheduling window.
  A scheduling window is a scheduling period consisting of control region and data region.
  Timing offset can be jointly encoded with resource allocation of NB-PDSCH
The timing offset between NB-PUSCH (carrying data) and NB-PDCCH is dynamically indicated in UL DCI
  UE assumes that NB-PDCCH carrying UL DCI schedules the NB-PUSCH (carrying data) in the next scheduling window.
The timing offset between NB-PUSCH (carrying only UL /AN) and NB-PDCCH is dynamically indicated in DL DCI.
  UE assumes that NB-PDCCH carrying DL DCI schedules the UL A/N transmission in the next scheduling window

## Slide 3: Appendix: Example of Scheduling window

## Slide 4: Appendix: Example of Scheduling window (cont.)