## Slide 1: WF on MCS/TBS table for NB-PDSCH
ZTE,
R1-161412
3GPP TSG RAN WG1 #84 meeting
St. Julian, Malta, 15th – 19th February 2016
Agenda item 7.2.1.1.3

## Slide 2
Background: Design Principals
  16QAM is not supported for NB-PDSCH.
Max of TBS is 680 bits
MCS table is based on the Rel-11 MCS table
    Decrease code rates of all selected R11 MCSs half so that the code rate of the highest MCS is slightly lower than 1/3.
    Pruned to SNR spacing of around 2 dB
Max of RUs for TBS is FFS

## Slide 3
Proposal -1
MCS table for NB-PDSCH
NB-IoT MCS index (LTE R11 MCS index) IMCS | Modulation order Qm | NB-IoT TBS index (LTE R11 MCS index) ITBS
0(0) | 2 | 0(0)
1(2) | 2 | 1(2)
2(4) | 2 | 2(4)
3(6) | 2 | 3(6)
4(8) | 2 | 4(8)

## Slide 4
Proposal -2
There are two options to decrease all code rates half
  Option 1: TBS table for NB-PDSCH by doubling
  RU numbers per column
ITBS | NRU |  |  |  |  | 
 | 2 | 4 | 6 | 8 | 10 | 12
0(0) | 16 | 32 | 56 | 88 | 120 | 152
1(2) | 32 | 56 | 120 | 176 | 208 | 256
2(4) | 56 | 120 | 208 | 256 | 328 | 392
3(6) | 88 | 176 | 256 | 392 | 504 | 600
4(8) | 120 | 256 | 392 | 504 | 680 | -

## Slide 5
Proposal -2 (cont.)
  Option 2: TBS table for NB-PDSCH by scaling
TBS [New_TBS = round((R11_TBS + 24)/2 - 24)]
ITBS | NRU |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0(0) | - | - | 16 | 32 | 48 | 64 | 76 | 92 | 100 | 116
1(2) | - | 24 | 60 | 76 | 92 | 116 | 136 | 152 | 176 | 200
2(4) | 16 | 48 | 92 | 116 | 152 | 192 | 232 | 264 | 304 | 336
3(6) | 32 | 76 | 116 | 184 | 240 | 288 | 344 | 392 | 456 | 504
4(8) | 48 | 116 | 184 | 256 | 328 | 392 | 472 | 536 | 616 | 680

## Slide 6
Parameter | Value
Scenario | AWGN
Antenna configuration | 1Tx, 1Rx
TBS | Refer to Option 1 TBS table
ITBS | 0, 1, 2, 3, 4
NRU | 1-6
Number of REs per RU | 104 (In-band)
Table C2 Parameters of link simulation
Appendix: Performance
Simulation assumption for Option 1 and 104REs per RU (In-band)

## Slide 7
Appendix: Performance
BLER performance for Option 1 and 104REs per RU (In-band)

## Slide 8
Appendix: Performance
Require SNR (@BLER=0.1) for Option 1 and 104REs per RU (In-band)

## Slide 9
Parameter | Value
Scenario | AWGN
Antenna configuration | 1Tx, 1Rx
TBS | Refer to Option 1 TBS table
ITBS | 0, 1, 2, 3, 4
NRU | 1-6
Number of REs per RU | 116 (Guard-band and Standalone)
Table C2 Parameters of link simulation
Appendix: Performance
Simulation assumption for Option 1 and 116REs per RU

## Slide 10
Appendix: Performance
BLER performance for Option 1 and 116REs per RU (Guard-band and Standalone)

## Slide 11
Appendix: Performance
Require SNR (@BLER=0.1) for Option 1 and 116REs per RU (Guard-band and Stand-alone)

## Slide 12
Parameter | Value
Scenario | AWGN
Antenna configuration | 1Tx, 1Rx
TBS | Refer to Option 2 TBS table
ITBS | 0, 1, 2, 3, 4
NRU | 1-10
Number of REs per RU | 104 (In-band)
Table C2 Parameters of link simulation
Appendix: Performance
Simulation assumption for Option 2 and 104REs per RU

## Slide 13
Appendix: Performance
BLER performance for Option 2 and 104REs per RU (In-band)

## Slide 14
Appendix: Performance
BLER performance for Option 2 and 104REs per RU (In-band)

## Slide 15
Appendix: Performance
Require SNR (@BLER=0.1) for Option 2 and 104REs per RU (In-band)

## Slide 16
Parameter | Value
Scenario | AWGN
Antenna configuration | 1Tx, 1Rx
TBS | Refer to Option 2 TBS table
ITBS | 0, 1, 2, 3, 4
NRU | 1-10
Number of REs per RU | 116 (Guard-band and Stand-alone)
Table C2 Parameters of link simulation
Appendix: Performance
Simulation assumption for Option 2 and 116REs per RU

## Slide 17
Appendix: Performance
BLER performance for Option 2 and 116REs per RU (Guard-band and Standalone)

## Slide 18
Appendix: Performance
BLER performance for Option 2 and 116REs per RU (Guard-band and Standalone)

## Slide 19
Appendix: Performance
Require SNR (@BLER=0.1) for Option 2 and 116REs per RU (Guard-band and Stand-alone)