## Slide 1: Way forward on sTTI structure
Ericsson, NTT DOCOMO, CATT, Mitsubishi Electric
R1-161420
Ag 7.3.4.2
RAN1 #84 Malta
February 15-19 2016

## Slide 2: Proposal
Following design assumptions are used for the study
  Alt 1.
    sTTI is assigned in FDM manner
  Alt 2.
    One or multiple set(s) of PRB pairs are allocated for sTTI operation for s(E)PDCCH in a subframe
      Note that s(E)PDCCH may not use all allocated resources
    One or multiple set(s) of PRB pairs are allocated for sTTI operation for sPDSCH in a subframe
    One or multiple set(s) of PRB pairs are allocated for sTTI operation for sPUSCH in a subframe
    One or multiple set(s) of PRB pairs are allocated for sTTI operation for sPUCCH in a subframe
    Further study how the sets are assigned to the UE
      Consider further whether one or multiple of the channels can be allocated by the same message

## Slide 3: Proposal
In this study, following aspects are assumed in RAN1.
  PSS/SSS, PBCH, PCFICH and PRACH, Random access, SIB and Paging procedures are not modified.
Following aspects are further studied in the next RAN1 meeting
  Note: But the study is not limited to them.
  Design of PUSCH DM-RS
    Alt.1: DM-RS symbol shared by multiple short-TTIs within the same subframe
    Alt.2: DM-RS contained in each sPUSCH
  HARQ for sPUSCH
    Whether/how to realize asynchronous and/or synchronous HARQ
  sTTI operation for SCells and LAA SCells