## Slide 1: WF on NB-PBCH Rate Matching and RE Mapping
Intel Corporation, ALU, ASB, MediaTek, Nokia, ZTE
3GPP TSG RAN WG1 Meeting #84 R1-161434
St Julian’s, Malta, 15th - 19th February 2016

## Slide 2: Background
In FDD mode, NB-PBCH is transmitted in subframe 0 in every radio frame
In FDD mode, NB-PBCH does not use the first 3 symbols in a subframe at least in in-band operation
For stand-alone and guard band operations, in the subframe transmitted NB-PBCH, the first 3 symbols contains no NB-PBCH
NB-PBCH is rate matched around 4 port LTE CRS location based on PCID from NB-SSS
  It is not precluded the PCID from NB-SSS is different from the LTE PCID
    Note that the PCID from NB-SSS and the LTE PCID indicate the same LTE CRS position
The time interval where MIB remains unchanged is 640 ms
NB-PBCH consists of 8 independently decodable blocks of 80 ms duration
From RAN1 point of views, NB-MIB can be 34-bit payload and has a 16-bit CRC

## Slide 3: NB-PBCH Rate Matching and RE Mapping
In FDD mode, after CRC attachment and channel coding, the NB-MIB is rate matched to E=1,600 bits denoted by e0, e1, …,eE-1 according to Section 5.3.1.3 in TS 36.212
The rate matched bits are scrambled with a sequence of length 1,600
  The scrambling sequence for the NB-PBCH is given in 7.2 of TS 36.211 and is initialized with the NB-IoT Physical Cell Identifier (PCI) in each radio frame fulfilling nf mod 64 = 0 where nf is the System Frame Number (SFN)
The modulated bits are mapped to resource elements in a frequency first, time second fashion
Within one NB-MIB TTI, the i-th block of 80ms duration, i=0,1,…,7, is used to transmit bits e200*i+j , j=0,1,…,199, i.e., identical symbols are transmitted in each subframe #0 within the i-th block

## Slide 4: Illustration of Proposal