## Slide 1: WF on NB-IoT msg3 transmission
Huawei, Hisi, CMCC, Ericsson
R1-161452
3GPP TSG RAN WG1 Meeting #84
St. Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.2.2

## Slide 2: Proposal
In extreme coverage level and extended coverage level, NB-PRACH resources indicate single tone msg3 transmissions.
In normal coverage level, separate NB-PRACH resources can be allocated for single tone msg3 transmissions and multi-tone msg3 transmissions
  Configuration can be broadcast in SIB
Introduce one IOT bit in msg3 signaling for the support of 15 kHz multi-tone UL transmissions
Network can schedule multi-tone msg3 transmissions if network has the knowledge of UE multi-tone transmission capability