## Slide 1: WF on the UE-SS Starting Subframe for eMTC
Nokia Networks, ALU, ASB, Ericsson, Panasonic, CATT
R1-161476
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Proposal
Modify the G array as follows:
  T=Rmax*G, G is from {1, 1.5, 2, 2.5, 3, 4, 5, 8, 10, reserved} for FDD, and {1, 2, 4, 5, 8, 10, 20, reserved} for TDD and the index of one element is given by the higher layer parameter mPDCCH-startSF-UESS.
A MPDCCH SS with repetitions that crosses over (SFN=0,nf=0), is not monitored by the UE.
At each (SFN=0, nf=0), the UE shall reset the starting SF used for the SS.