## Slide 1: Discussion on consistent pathloss model between below 6 GHz and above 6 GHz
Samsung
R1-164807
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.2.1

## Slide 2: Background
Detailed channel modelling for above 6 GHz was almost completed in RAN1 #84bis
  Currently, the new pathloss model in TR38.900 is applicable from 0.8 GHz up to 73 GHz
For LTE system evaluation, 3D-SCM [TR36.873] used for below 6 GHz
  The pathloss model in 3D-SCM is applicable from 2 GHz up to 6 GHz
It seems necessary to discuss how to keep the consistency between below 6 GHz channel model and above 6 GHz model
Also, need to define the clear applicable frequency range of the new channel model  Proposal in R1-164616

## Slide 3: Possible Solution to keep consistency between models, #1
If two incompatible pathloss models are adopted according to Alt 1 in R1-164616, pathloss discontinuities occur at 6 GHz.
(3 dB gap and 7.5 dB gap at 6 GHz for LoS and NLoS, respectively)
[Possible Solution #1] Patch smoothly between two models
  It may also require to modify the current pathloss model for below 6 GHz
  because of the higher pathloss in the current below 6 GHz model due to higher γ (=2.6)

## Slide 4: Patched two pathloss models in transition band
By introducing transition frequency band to patch two models, three pathloss models can reduce the discontinuity at 6 GHz
Considerations for deriving frequency bands
  No change on 3D-SCM model, at least around 2 GHz
  For smooth transition between <6GHz and >6GHz, some range near sub-6 GHz needs to be modified
  For simple model extension, α/β/γ parameters are adjusted for patching two models
  γ in transition is optimized to match models at 50 m for smaller gap in near distance
For 2 GHz ~ 10 GHz range, new transition models are derived

## Slide 5: Summary of Possible Solution #1
If two incompatible pathloss models are adopted for below 6 GHz and above 6 GHz, transition range in frequency is required to avoid pathloss discontinuities occur at 6 GHz.
In UMi, three band models are proposed
  3D-SCM model only for 2 GHz
  Transition model from 2 GHz up to 10 GHz
  5GCM model for above 10 GHz

## Slide 6: Possible Solutions to keep consistency between models, #2
As following observations in R1-164806, Alt. 2 in R1-164616 can simply solve the consistency issue between pathloss models
The new pathloss model is proposed based on the dataset including both below and above 6 GHz, then it is natural to apply the new model for all valid frequency range
[Possible Solution #2]
  Apply the new pathloss model to the range of 0.5 – 100 GHz solely for NR system evaluation
Solution #2 is preferable, because
  It is much simpler approach
  Transition model in Solution #1 is not verified with measurement campaigns
    Higher or lower γ values in transition model
  Also Solution #1 needs to modify the current pathloss model near sub-6 GHz

## Slide 7: Conclusion
Observation:
  Discontinuity occurs at 6GHz using two incompatible pathloss models
  There is two possible solutions to keep consistent pathloss
    Patch between two models
    Apply new model to all valid frequency range
Proposal 1:
  Considering the simplicity and the consistency in pathloss models, Solution #2 should be taken into TR38.900
Proposal 2:
  Alt 2 : New channel model in TR38.900 is applicable to 0.5 - 100 GHz in R1-164616 should be down-selected

## Slide 8: Appendix : UMi LoS Model
For 2GHz, 3D-SCM model is used
For 2~10 GHz, the new transition model is derived
For f > 10 GHz, 5GCM model is used
  Then, the breaking-point model is applied for each band

## Slide 9: Appendix : UMi NLoS Model
For 2GHz, 3D-SCM model is used
For 2~10 GHz, the new transition model is derived
For f > 10 GHz, 5GCM model is used