## Slide 1: NR Numerology Design Principles
Qualcomm Proprietary and Confidential
3GPP TSG-RAN WG1 #85 R1-165112
23th – 27th May 2016
Nanjing, China
Agenda item: 7.1.4

## Slide 2: Outline
Design principles
Motivation for not using backward (LTE) compatible numerology
  Better low latency / TTI multiplexing
  Better long CP support
  Lower mMTC complexity
Resolving concerns on new numerology
  Multi-standards RRH consideration
  NB-IOT coexistence
Way forward
Appendix
  List of draft contributions to RAN1 #85 in Nanjing China (May 23-27)
  Simulation assumptions/results

## Slide 3: Design Principles
Power of 2 numerology scaling design is a general design principle
5G air interface is designed to scale for different latency and granularity
  Following principles seem to be agreeable to most companies
    power of 2 scaling of subcarrier spacing
    power of 2 subframes per 1 ms
  Natural extension of principles 1, 2
    power of 2 uniform symbols per subframe (also power of 2 symbols per 1ms)
    CP duration is scalable with numerology for different deployment scenarios
  Hardware reuse 
    NR subcarrier spacing is LTE tone spacing x N/D for small N and D
      E.g., f0 = 17.5KHz = 7/6 * 15KHz

## Slide 4: Why not backward (LTE) compatible numerology?
Feature\RAT | LTE | NR
Low latency TTI multiplexing | 7-symbol per slot NOT scalable to short TTI gracefully | Graceful scaling of TTI achieved via: 1) Subcarrier spacing scaling 2) Number of symbols scaling
Narrowband Sub-RAT | Non-uniform symbol duration Forcing much higher sampling rate and FFT size than necessary | Uniform symbol duration Low complexity design scalable to massive number of devices
Long CP Support | Higher overhead Almost never used except for eMBMS | Scaled numerology to keep low overhead Strong candidate to replace LTE ECP
NR is the opportunity to remove LTE legacy limitations from day one
Next few slides will provide details on each of the 3 areas

## Slide 5: Low Latency (1/2)
Two different approaches to achieve shorter TTIs
  Scaling subcarrier spacing by 2^K: better pipeline processing
  Scaling the number of symbols per TTI by 1/2^K: Robustness
TTI multiplexing is inefficient in LTE due to 7-symbol numerology
  Symbol scaling does not work, lead to half symbol

## Slide 6: Low Latency (2/2)
Scaling number of symbols is one simple way of achieve latency reduction with robust performance against DS
Power of 2 scaling in SCS and number of symbols ensures:
  The same TTI duration could be achieved via 1) SCS scaling and 2) number of symbols scaling
Simulation assumptions: link

## Slide 7: Narrowband Sub-RAT
NB-IOT has to sample at 1.92 MHz due to LTE un-even symbol duration
NR mMTC mode have much lower sampling rate and FFT complexity

## Slide 8: Long CP Support – 1 to 1.5 dB Gain over LTE ECP
Performance of long CP by scaling numerology is more efficient for most scenarios (RAN4 MBSFN channel model)
Open to other ECP options, such as 6 symbol per 0.5ms or different FFT size if special use case exists
Simulation assumptions: link
1.5 dB gain
1 dB gain

## Slide 9: ZTE numerology proposal
  Non-power-of-2 FFT size
  Same sampling rate as LTE
    May not be fundamental implementation constraint
  ECP is achieved by going to a different SCS and keeping 16 symbols per ms
    FFS: comparison with 1) scaled CP 2) different number of symbols ECP
 | LTE | LTE | Qualcomm (17.5 kHz) | ZTE NCP | ZTE ECP
 | Normal CP | ECP | Scalable CP | fixed sampling rate | fixed sampling rate
SC spacing [kHz] | 15 | 15 | 17.5 | 17.07 | 21.33
OFDM symbol length [us] | 66.67 | 66.67 | 57.14 | 58.6 | 46.87
CP-length [us] | 5.2/4.7 | 16.67 | 5.36 | 3.9 | 15.63
Nr of symbols per subframe | 14 | 12 | 16 | 16 | 16
subframe length | 1ms | 1ms | 1ms | 1ms | 1ms
sampling rate [Mhz] | 30.72 | 30.72 | 35.84 | 30.72 | 30.72
CP overhead | 7% | 20% | 8.60% | 6.00% | 25%
Note | FFT = 2048 | FFT = 2048 | FFT=2048 | FFT=1800 | FFT = 1440

## Slide 10: Multi-Standards Radio Considerations
Subcarrier spacing is chosen to be LTE tone spacing x N/D for small N and D
  Enables XO reuse for multi-RAT eNB and UE
Some companies raised concern on different sampling rate impact to MSR RRH
  Concern:
    Different sampling rates between NR and LTE is a showstopper for base-band only upgrade for NR without touching RRH
  However, concerns could be mitigated by
    If legacy fronthaul (e.g., CPRI) is used, baseband can simply resample the RF samples at the CU without modifying RU
    If new (5G) fronthaul is used, RU will be upgraded anyway, no such issue

## Slide 11: NR and NB-IOT Coexistence
Standalone NB-IOT could coexist with LTE/UMTS/GSM with uncoordinated deployment without problem (based on RAN4 study)
NR is designed for forward compatibility, which by definition supports “Inband” NB-IOT
  Optimization is needed even for 15 KHz SCS, e.g., RB definition
GB/inband on the edge NB-IOT and NR coexistence is clearly supported

## Slide 12: System-level sim of NB-IOT and NR coexistence
Coexistence impact is very minor and only limited to high geometry
NB-IOT to NR impact is mainly on the 1st adjacent RB and limited to high geometry
NR to NB-IOT impact is only at high geometry (negligible for low NB-IOT data rate)
System-level sim results are much better than standalone coexistence due to coordinated deployment

## Slide 13: Way Forward
In RAN1 #85, RAN1 could agree on the scaling methodology in frequency:
  The subcarrier spacing for the NR scalable numerology should scale as
    fsc = f0 * 2m
    where
      f0 is FFS
      m is an integer chosen from a set of possible values
In RAN1 #86, RAN1 could agree on the specific values of
  f0 and m

## Slide 14: NR Numerology Discussion in 3GPP (1/2)
Chairman Notes from RAN1 April 2016 Meeting
  For NR, it is necessary to support more than one values of subcarrier-spacing
    Values of subcarrier-spacing are derived from a particular value of subcarrier-spacing multiplied by N where N is an integer
      Alt.1: Subcarrier-spacing values include 15 kHz subcarrier-spacing (i.e., LTE based numerology)
      Alt.2: Subcarrier-spacing values include 17.5 kHz subcarrier-spacing with uniform symbol duration including CP length
      Alt.3: Subcarrier-spacing values include 17.06 kHz subcarrier-spacing with uniform symbol duration including CP length
      Alt.4: Subcarrier-spacing values 21.33 kHz
      Note: other alternatives are not precluded
      FFS: exact value of a particular value and possible values of N
Observations:
  RAN1 agreed that all SCS should be derived from some fundamental SCS f0
  Alt. 1/2/3/4 are the proposals for the fundamental f0
  Alt. 2/3/4 belongs to the family of numerologies with 2m symbols per/TTI
Numerology Decisions are Critical for Frame Structure Design and Product Implementation

## Slide 15: NR Numerology Discussion in 3GPP (2/2)
Chairman Notes from RAN1 April 2016 Meeting
  RAN1 will continue further study and conclude between following alternatives in the next meeting
  - Alt. 1:
    The subcarrier spacing for the NR scalable numerology should scale as
    fsc = f0 * 2m
    where
      f0 is FFS
      m is an integer chosen from a set of possible values
  - Alt. 2:
    The subcarrier spacing for the NR scalable numerology should scale as
    fsc = f0 * M
    where
      f0 is FFS
      M is an integer chosen from a set of possible positive values
Observations:
  Majority of RAN1 agreed on the scaling factor N being a power of 2
  Some companies would like to keep the scaling factor flexible

## Slide 16: Appendix

## Slide 17: List of Contributions to RAN1 #85
7.1.4 NB-IOT Coexistence Analysis for NR Numerology
7.1.4 Long DS channel evaluation
7.1.4 TTI multiplexing and Forward Compatibility Analysis for NR numerology
7.1.4 NR Numerology Considerations for eMBB and mMTC

## Slide 18: Simulation parameters TTI Scaing (back)
Simulation parameter | Value
Physical channels present | PDSCH
coding | 3GPP Turbo
Link Adaptation | Yes
Subframe duration | 125 us
Demapper | LMMSE
HARQ number of transmissions | 4 (RV: 0,1,2,3)
Fading model | TDL
Precoding | Open loop precoding
Channel Model | TDL-C (DS: 300 and 1000 ns)
Doppler | 5Hz
Num Layers | 2
Sim Profile | 17.5 KHz | 35 KHz | 70 KHz | 140 KHz
Tones spacing (kHz) | 17.5 | 35 | 70 | 140
FFTSize | 2048 | 2048 | 2048 | 2048
Sample Rate (kHz) | 35840 | 71680 | 143360 | 286720
CP (us) | 5.3571 | 2.6786 | 1.3393 | 0.6696
# active tones/symbol | 1152 | 576 | 288 | 144
Active PDSCH BW (kHz) | 20160 | 20160 | 20160 | 20160
Symbol Length (us) | 62.5 | 31.25 | 15.626 | 7.8125
CPLength (samples) | 192 | 192 | 192 | 192
Symbol Length (samples) | 2240 | 2240 | 2240 | 2240
CPRatio (CP/FFT) | 0.09375 | 0.09375 | 0.09375 | 0.09375

## Slide 19: Simulation parameters MBSFN Scenario (back)
Simulation parameter | Value
Physical channels present | PDSCH
coding | 3GPP Turbo
Link Adaptation | Yes
Subframe duration | 1000 usec
Number of interlaces | One
Demapper | MMSE
HARQ Transmissions | 4 (RV: 0,1,2,3)
Fading model | 3GPP eMBMS Channel Model
Transmission Mode | SIMO
Channel Model | TDL-C (DS: 300 and 1000 ns)
Doppler | 200Hz, 600Hz
Sim Profile | LTE ECP | 17.5 KHz | 8.75 KHz | 4.375 KHz
Tones spacing (kHz) | 15 | 17.5 | 8.75 | 4.375
FFTSize | 2048 | 2048 | 2048 | 4096
Sample Rate (kHz) | 30720 | 35840 | 17920 | 17920
CP (us) | 16.6667 | 5.3571 | 10.7143 | 21.4286
# active tones/symbol | 672 | 576 | 1152 | 2304
Active PDSCH BW (kHz) | 10080 | 10080 | 10080 | 10080
Symbol Length (us) | 83.3333 | 62.5 | 125 | 250
CPLength (samples) | 512 | 192 | 192 | 192
Symbol Length (samples) | 2560 | 2240 | 2240 | 2240
CPRatio (CP/FFT) | 0.25 | 0.09375 | 0.09375 | 0.09375

## Slide 20: Table for MBSFN channel model
From 36.101, Table B.2.6-1

## Slide 21: Link-level ICI of NB-IOT and NR (17.5KHz) Coexistence
NB-IOT and NR coexistence (GB or inband on the edge of the carrier BW)
SINR ceiling from NR to NB-IOT ICI is around 26dB
SINR ceiling from NB-IOT to NR ICI is around 18dB for the 1st adjacent RB and goes up to >30dB within 3~4RBs