## Slide 1: WF on mobility enhancement for spatial consistency
Intel, Ericsson, AT&T, ETRI, Huawei, HiSilicon, KT Corporation, Nokia, NTT DOCOMO, Qualcomm, Samsung
R1-165234
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.2.3.2

## Slide 2: Background
Spatial consistency modelling has been agreed in R1-163475/R1-161726
It has been observed by R1-162244, R1-162389 that agreed spatial consistency modelling can cause the delay/angle of the weak clusters varying faster than physically allowed
  This maybe harmful to simulate mobility (UE position changes during the simulation)
Two enhancements are possible to address this issue:
  R1-163480: temporal update of channel cluster delay/power/angle based on UE geometry
  R1-163248: change the channel cluster generation steps from delay/power/angle to delay/angle/power
“Cluster specific sign for AoD/AoA/ZoD/ZoA in step 7 shall be generated once per simulation drop” in the current TP assuming UE position change during the simulation.
  It does not mention whether it is spatially consistent in one drop

## Slide 3: Proposal
Proposal 1: Both alternatives are captured in TR 38.900
  Alternative 1: based on R1-163480, details described in the following slides
  Alternative 2: based on R1-163248, details described in the following slides
Proposal 2: Modify the below text by adding the red text into the current TP
  The cluster specific random variables include:
    Cluster specific random delay in step 5;
    Cluster specific shadowing in step 6; and
    Cluster specific offset for AoD/AoA/ZoD/ZoA in step 7.
    Cluster specific sign for AoD/AoA/ZoD/ZoA in step 7
  The procedure shall apply to each cluster before sorting the delay. Cluster specific sign for AoD/AoA/ZoD/ZoA in step 7 shall be generated once kept unchanged per simulation drop if UE position changes during simulation. The ray specific random variables include:

## Slide 4: Alternative 1
When UE position is changed in simulation, the temporal channel evolution can be modelled as:
  For t0=0 when UE is dropped into the network, use R1-163475/R1-161726 to generate channel cluster power/delay/angles
  Update channel cluster power/delay/angles at t0+t based on UE channel cluster power/delay/angles, moving speed and direction at t0
    Cluster delay:
    Cluster power: using step 6 with cluster delay
    Cluster departure angle:
    Cluster arrival angle:

## Slide 5: Alternative 1
    =v(,0)
    v is UE moving speed in the horizontal plane
    C is speed of light
    is UE moving direction in the horizontal plane
    is 2D distance between Tx/Rx; is 3D distance between Tx/Rx
    , , , are cluster specific reflection surface angles;
      for LoS path, set to 0;
      for NLoS clusters,
        Generate using spatially consistent random numbers with uniform distribution U(-180, 180) and 50m correlation distance for , ,
        Generate using spatially consistent random numbers with uniform distribution U(-90, 90) and 100m correlation distance for ,

## Slide 6: Alternative 2
Modify steps 5,6, and 7 to include the following procedure:
  Step 5: Generate delays .
    Delays are drawn randomly from a uniform distribution. Calculate
    where is the maximum delay (), Xn ~ uniform(0,1), and cluster index n = 1,…,N.
    The autocorrelation distance of Xn is where is the speed of light
  Step 6: Generate arrival angles and departure angles for both azimuth and elevation.
    Calculate
    where is the maximum angle (), Yn ~ uniform(0,1), and cluster index n = 1,…,N.
    This step is repeated independently for AOD, AOA, ZOD, and ZOA with corresponding maximum angles
    The autocorrelation distance is = for AOD, ZOD, and [50m] for AOA,ZOA
    Offset angles etc are applied as before but not until cluster powers have been calculated
  Step 7: Generate cluster powers P.
    Cluster powers are calculated assuming a single slope exponential power profile and Laplacian angular power profiles. The cluster powers are determined by
    where Zn ~ N(0, z ) (autocorrelation distance same as for shadow fading) is the per cluster shadowing term in [dB].