## Slide 1: WF on frequency correlation
TSG-RAN WG1 #85 R1-165481
Nanjing, China, May 23 – 27, 2016
Source: Ericsson, ETRI, Telstra
Agenda Item: 7.2.1
Document for: Discussion, Decision

## Slide 2: Background
To support simulations with multiple sites, base stations, UEs, and frequencies, some clarification of how these links are correlated is needed
Some new procedures may be needed to support new model features
  Frequency consistency (multi-band simulations)
  Spatial consistency (additional parameters may be correlated)
No procedure defined in 36.873 or 38.900 for correlations between links involving the same BS and UT at different frequencies

## Slide 3: Background
In 38.913 v0.3.0, scenario descriptions for NR evaluations are provided
For Dense Urban:
Layout | Two layers: - Macro layer: Hex. Grid - Micro layer: Random drop Step 1 NOTE3: Around 4GHz in Macro layer Step 2 NOTE3: Both Around 4GHz & Around 30GHz may be available in Macro & Micro layers (including 1 macro layer, macro cell only)

## Slide 4: Correlation between links at different frequencies Steps 1,2
UE indoor/outdoor state and LOS/NLOS state should be the same
Position of UE and of blockers should be the same
Path loss is different
Antenna configurations may be different
Proposal 1: Step 1 is identical for all frequencies, except:
  1d Antenna patterns and array geometries
  1g System centre frequency and bandwidth
Proposal 2: Step 2 is identical for all frequencies
Proposal 3: If blocking is modeled, the positions of blockers are the same for all frequencies
  Note: The blocking loss may be different
BS
UE2
f1
f2
BS
UE1
f1
f2
Blocking object
Building

## Slide 5: Correlation between links at different frequencies Step 4
Shadow fading, angular spread, and delay spread are determined partially by environment and partially by possibly frequency-dependent propagation such as transmission, reflection, diffraction
  A fairly large degree of correlation over frequency can be expected
Proposal 4: Step 4 is identical for all frequencies, except for possibly frequency-dependent scaling of e.g. delay spread and angular spreads according to the LSP tables
BS
UE
f1
f2

## Slide 6: Correlation between links at different frequencies Steps 5-7
Measurements have shown that cluster delays and angles are very similar over frequency
  Examples given in the Appendix
  Natural and intuitive since delays and angles depend on geometry of environment
  Powers may sometimes be different, since reflection/diffraction/scattering coefficients etc may be frequency dependent
Proposal 5: The cluster delays and angles resulting from steps 5-7 are same for all frequency bands
Proposal 6: Per-cluster shadowing (Zn in step 6) is independent for different frequency bands
Proposal 7: Cluster powers in step 6 are derived from the delay and angle spreads and may be frequency-dependent
BS
UE
f1
f2

## Slide 7: Correlation between links at different frequencies Steps 8-11
Fast fading is expected to be uncorrelated between different frequency bands
Proposal 8: Steps 8-11 are independent for different frequency bands
BS
UE
f1
f2

## Slide 8: Summary
Proposal 1: Step 1 is identical for all frequencies, except:
  1d Antenna patterns and array geometries
  1g System centre frequency and bandwidth
Proposal 2: Step 2 is identical for all frequencies
Proposal 3: If blocking is modeled, the positions of blockers are the same for all frequencies
  Note: The blocking loss may be different
Proposal 4: Step 4 is identical for all frequencies, except for possibly frequency-dependent scaling of e.g. delay spread and angular spreads according to the LSP tables
Proposal 5: The cluster delays and angles resulting from steps 5-7 are same for all frequency bands
Proposal 6: Per-cluster shadowing (Zn in step 6) is independent for different frequency bands
Proposal 7: Cluster powers in step 6 are derived from the delay and angle spreads and may be frequency-dependent
Proposal 8: Steps 8-11 are independent for different frequency bands

## Slide 9: Appendix: Examples from measurements

## Slide 10: T. Jämsä, V. Hovinen, A. Karjalainen, J. Iinatti, “Frequency dependency of delay spread and path loss in indoor ultra-wideband channels”, in Proc. of IET UWBSTA, 2006
First, second, and third cluster at same delay for all frequency bands

## Slide 11: R. Müller, S. Häfner, D. Dupleich, et al., “Simultaneous multi-band channel sounding at mm-wave frequencies”, in Proc. EuCAP 2015
All clusters have same delays at both frequency bands
  Cluster powers may be frequency-dependent

## Slide 12: Weiler, “Simultaneous millimeter-wave multi-band channel sounding in an urban access scenario”, in Proc. EuCAP 2015
Prominent clusters at identical delays
  Cluster powers may be frequency-dependent

## Slide 13: R1-163254 “On the frequency dependence of LSPs”, Ericsson, Busan, April 2016
Very similar cluster DoAs in azimuth, zenith, and delay
In some cases, cluster powers are frequency-dependent
Fig. 2. Measured directional power spectra. Here, zero degrees in azimuth correspond to the negative x direction in Fig. 1.
LOS 5.8 GHz
LOS 14.8 GHz
LOS 58.7 GHz
Power relative to free space at 1.5 m [dB]
Power relative to free space at 14 m [dB]
NLOS 5.8 GHz
NLOS 14.8 GHz

## Slide 14: J. Vehmas, J. Järveläinen, S. Nguyen, R. Naderpour, and K. Haneda, "Millimeter-Wave Channel Characterization at Helsinki Airport in the 15, 28, and 60 GHz", submitted to VTC-Fall 2016.
Prominent clusters at same delays
  Cluster powers may be frequency-dependent