## Slide 1: WF on PRACH for Enhanced LAA
Ericsson
3GPP TSG RAN WG1 #85 R1-165498
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.4
Document for decision

## Slide 2: Background
The WID objective was to specify support for PRACH if needed
RAN1 agreed to support non-contention based PRACH in the following agreement in RAN1#84
Agreements:
  Contention based PRACH transmission on LAA Scell is not supported in Rel-14
  Non-contention based PRACH transmission on LAA Scell is supported in Rel-14 subject to LBT
  FFS: PRACH duration up to 1msec is supported
  FFS: A UL transmission burst containing PRACH without other UL channel immediately follows a single idle observation interval of at least 25 micro sec
  FFS: new PRACH waveform

## Slide 3: Background
In the discussions, it was recognized that many use cases do not need the PRACH
Four different waveforms have been proposed for PRACH
  Repetition of legacy waveform in frequency
  Interlace based waveform
  Legacy waveform incorporated into an interlaced structure
  Contiguous repetition of 6 PRBs

## Slide 4: Proposal
Capture the following Conclusion in the Chairman’s notes:
Conclusion:
  Enhanced LAA can operate without PRACH
  PRACH is useful in some use cases
  The following approaches have been identified for the PRACH
    Repetition of legacy waveform in frequency
    Interlace based waveform
    Legacy waveform incorporated into an interlaced structure
    Contiguous repetition of 6 PRBs