## Slide 1: Way forward on processing timing reduction for sTTI
Ericsson
R1-165524
AI 6.2.10.1
3GPP RAN WG 1 #85
23rd – 27th May2016, Nanjing , P.R. China

## Slide 2: Background
The system evaluation provided to RAN1 #85 shows that even if the processing time cannot be linearly scaled with TTI length, short TTI significantly improves data rate
Maximum TA affects the minimum delay between UL grant reception and UL data transmission and between the DL data reception and DL HARQ feedback transmission

## Slide 3: Proposal
It is recommended to limit the maximum TA
  Example value can be half of the current TA value, i.e. 0.33ms
The following options are considered for DL and UL processing time reduction for short TTI operation
  Option1:
    Legacy processing time linearly downscaled with TTI length
      The timing for UL grant to UL data or for DL data to DL HARQ :
        n+4 sTTI for all TTI lengths
  Option 2:
    Higher processing time than the legacy processing time linearly downscaled with TTI length
      The timing for UL grant to UL data or for DL data to DL HARQ :
        n+8 sTTI in case of 2 os TTI
        n+6 sTTI in case of 4 os TTI
        n+5 sTTI in case of slot based TTI
  Option 3
    Use configurable UE-specific timing for UL grant to UL data or for DL data to DL HARQ
      The k value in n+k may depend on UE capability and/or TA value
      FFS: k can be fixed, semi-static, or dynamic