## Slide 1: WF on evaluaton assumptions for high speed train scenario
CMCC, CATT, Huawei, CATR, China Unicom, ZTE,
3GPP TSG RAN WG1 Meeting #85 R1-165576 Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2

## Slide 2: Background
In R1-163887, some evaluation assumptions for the high speed train scenario were agreed, some bracket parts and FFS parts need further discussion and decision. More clarifications and detailed evaluation parameters are needed.

## Slide 3: Proposal
Linear BS placement along the rail track
Macro only layout is prioritized for evaluation
Carrier frequency: 4GHz
  Other lower frequency options such as around 2GHz are not precluded if required.
Both SFN scenario and non-SFN scenario are considered.

## Slide 4: Proposal
SFN scenario parameters
Non-SFN scenario parameters
Parameter | Value
Distance between RRH and Railway track | 100m
Distance between sites(2RRHs on 1 site) | 1732m
Num of RRHs connected to one BBU | 6
Parameter | Value
Distance between RRH and Railway track | 100m
Distance between sites(2RRHs on 1 site) | 1732m
Num of RRHs connected to one BBU | 2

## Slide 5: Proposal
SFN model: First priority
Non-SFN model

## Slide 6: Proposal
Other evaluation parameters
Parameter | Value
Train length | 400m
Num of users per train | 1000
UE dropping | Uniform in train
UE height (compared to railway track)1) | 2m
UE distribution | 300 for non-full buffer (1000 users with 30% activity rate); 20 for full buffer
Channel model | ITU rural as starting point Note : when 5G CM is available, 5GCM can be used
Note 1: UE height refers to the vertical distance between the UE and the railway track, which is the sum of train floor height over the track (roughly 1.3m) and the UE height over the train floor (roughly 0.7m) assuming users are sitting.
The azimuth direction of the main beam peak is to be determined by choosing the direction that provides optimal geometry.

## Slide 7: Proposal
KPI
  Spectrum efficiency, area traffic capacity, user experienced data rate, system handover capability
System level and link level evaluation are needed
  9 site(3BBU) wrap-around model for SFN as in page 5
  9 site(9BBU) wrap-around model for non-SFN as in page 5
NR RAN1 technologies that need to consider high speed impact
  Numerology, MA, MIMO