## Slide 1: WF on Scalable Numerology Symbol Boundary Alignment
Qualcomm, ZTE, ETRI, NEC, OPPO , Panasonic, DoCoMo, Deutsch Telecom, Convida Wireless, [MTK], [SPRINT], [Interdigital]
3GPP TSG RAN WG1 #85 R1-165583
Nanjing, China
23th – 27th May 2016
Agenda item:7.1.4
Document for decision

## Slide 2: Scaled numerology have alignment with long symbol boundary
f1 = 2 * f0
Alt 1, every two symbols of f1 numerology is aligned with symbol boundary of f0 numerology
Alt 2, every two symbols of f1 numerology is NOT aligned with symbol boundary of f0 numerology
f0 numerology
f1 numerology w/ symbol
boundary alignment
f1 numerology w/o symbol
boundary alignment

## Slide 3: Proposal
For scaled numerology Fs = F0*M, (where Base numerology contains N symbols per ms and scaled numerology contains N*M symbols per ms)
  Each symbol length (including CP) of base numerology (w/ SCS = F0) equals the sum of the corresponding M symbols of scaled numerology (w/ SCS = Fs)
  Each symbol may not necessarily be of the same length (e.g. in LTE numerology, symbol0 is long than symbol 1, 2, … 6)
  Multiple CP durations per each numerology is not precluded:
    For each CP family (NCP or ECP), each symbol length (including CP) of base numerology (w/ SCS = F0) equals the sum of the corresponding M symbols of scaled numerology (w/ SCS = Fs)
Example:

## Slide 4
Background

## Slide 5: Benefits of symbol boundary alignment
Benefits:
  Low latency TDM numerology multiplexing
  Better interference management
    Interference from short symbol numerology to long symbol numerology is contained in one symbol
  Less implementation complexity
  No obvious reason not to do

## Slide 6: Symbol boundary alignment for low latency numerology multiplexing
FDM-ing UEs of different numerology:
TDM-ing UEs of different numerology:
  Symbol-boundary alignment (at the smallest SCS symbol level) enables symbol-level numerology multiplexing:
Low latency could be achieved by TDM compared with FDM