## Slide 1: WF on system information and idle mode reception for eMBMS enhancements
Qualcomm, EBU, BBC, Ericsson
R1-165615
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 6.2.5

## Slide 2: Background
In RAN#71 a new work item named “eMBMS enhancements for LTE” was approved with the following features:
  Specify means of using a longer CP
  Specify means of using subframes 0, 4, 5, 9 (FS1) and 0, 1, 5, 6 (FS2) for MBSFN
  Specify means of configuring MBSFN subframes without a unicast control region and CRS
  Study support for standalone eMBMS carrier
  Study support of multi-carrier eMBMS/unicast from non-collocated and
  Study solutions where a UE can receive TV transport without being authenticated

## Slide 3: Proposal 1
A UE can receive eMBMS service in idle mode from a cell with increased number of MBSFN subframes per radio frame
  This is the same as legacy eMBMS operation.
  FFS modification of idle mode procedures (e.g. paging)

## Slide 4: Proposal 2
The necessary SIBs to enable eMBMS reception are transmitted over the cell with increased number of MBSFN subframes per radio frame.
For the case where the eMBMS cell with increased number of MBSFN subframes per radio frame is accessed as an SCell, the UE obtains SIB1 and SIB2 from higher layers, and SIB13 from the Scell
  This is the same as legacy eMBMS operation.

## Slide 5: Proposal 3
The synchronization and system information for a cell with increased number of MBSFN subframes per radio frame is transmitted over subframes with non-MBSFN numerology (15kHz)
  PSS and SSS follow legacy structure
    FFS possible changes to indicate non-backward compatible cell
  PBCH follows legacy structure
    FFS possible enhancements to overcome higher periodicity of PBCH
    FFS changes in payload or structure to indicate non-backward compatible cell
  SIBs are transmitted over PDSCH scheduled with PDCCH CSS
    FFS new predefined transmission instances for SIB1
    FFS enabling transmission of multiple SIBs over the same subframe
The non-MBSFN subframes used for PSS/SSS/PBCH/SIBs are transmitted with a periodicity of X and a length of Y
  Similar design as Rel 13 DRS
  FFS values of X and Y
  Non-MBSFN subframes used for PSS/SSS/PBCH/SIBs have a unicast control region and may carry PDCCH and PDSCH
  This does not preclude additional non-MBSFN subframes outside of this set of non-MBSFN subframes