## Slide 1: WF on NR forward compatibility
Huawei, HiSilicon
3GPP TSG RAN WG1 #85 R1-165628
Nanjing, China, May 23 - 28, 2016
Agenda item: 7.1.1

## Slide 2: Background
Phase 1 and later phases of NR should be designed with the following principles to ensure forward compatibility and compatibility of different features:
  Strive for
    Maximizing the amount of time and freq. resources that can be flexibly utilized or that can be left blanked without causing backward compatibility issues in the future
      Blank resources can be used for future use
    Minimizing transmission of always-on signals
    Confining signals and channels for physical layer functionalities (signals, channels, signaling) within a configurable/allocable time/freq. resource

## Slide 3: Proposals
Forward compatibility of NR shall ensure smooth introduction of future services and features with no impact on the access of earlier services and UEs
  Multiplexing different numerologies within a same NR carrier bandwidth (from the network perspective) is supported
  Reference signal for synchronization and transmission of MIB is not in a fixed frequency location within a NR carrier bandwidth (from the network perspective).
    The frequency location of MIB is derived from the reference signal for synchronization (e.g. the same frequency location)
  Avoid tying multiple parameters to a same parameter and rely more UE specific parameters as much as possible
  Common design should be aimed for various link directions in NR, e.g. downlink, uplink, sidelink, backhaul link