## Slide 1: Way Forward on evaluation methodologies
LG Electronics,
3GPP TSG RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.2
R1-165634

## Slide 2: Background
Main KPIs for mMTC in the TR38.913[1] are as follows :
  7.10 Coverage
    "Maximum coupling loss" (MCL) in uplink and downlink between device and Base Station site (antenna connector(s)) for a data rate of [X bps], where the data rate is observed at the egress/ingress point of the radio protocol stack in uplink and downlink.
    The target for coverage should be [164dB].
  7.11 UE battery life
    UE battery life can be evaluated by the battery life of the UE without recharge. For mMTC, UE battery life in extreme coverage shall be based on the activity of mobile originated data transfer consisting of [TBD bytes] UL per day followed by [TBD bytes] DL from MCL of [TBD] dB, assuming a stored energy capacity of [TBD].
    The target for UE battery life should be [15 years].
  7.17 Connection density
    Connection density refers to total number of devices fulfilling specific QoS per unit area (per km2). QoS definition should take into account the amount of data or access request generated within a time t_gen that can be sent or received within a given time, t_sendrx, with x% probability.
    The target for connection density should be 1 000 000 device/km2 in urban environment.
    3GPP should develop standards with means of high connection efficiency (measured as supported number of devices per TRP per unit frequency resource) to achieve the desired connection density.

## Slide 3: Background
Agreements on evaluation metrics for SLS made in RAN1 #84bis meeting captured from R1-163560 are as follows :
  For SLS, the following are used as evaluation metrics
    eMBB: TRP spectrum efficiency and 5th percentile user spectrum efficiency; user experienced data rate and area traffic capacity; signaling overhead
    mMTC: Connection density with “connection efficiency” reported; latency for infrequent small packets; signaling overhead
    URLLC: Reliability for a target latency
However, it is not so clear that the definition of the evaluation metrics for mMTC/URLLC and how they fit in the SLS
Other metrics for mMTC need to be clarified for RAN1 evaluation

## Slide 4: Proposal
RAN1 should discuss the main KPIs per usage scenario, i.e. eMBB, mMTC and URLLC and decide
  which KPIs are to be evaluated in RAN1 and focus on those KPIs for evaluation
  evaluation method and evaluation metrics per KPIs which will be evaluated in RAN1

## Slide 5: Proposal
At least following KPIs for mMTC should be evaluated in RAN1
  Coverage
  Connection density
  UE battery life
Evaluation methods and relevant evaluation metrics per KPIs for mMTC in RAN1 are as follow:
  Coverage is evaluated by link budget
  Connection density is evaluated by SLS and analysis
    In SLS, evaluation metric for connection density is connection efficiency
  UE battery life is evaluated by analysis
    Statistics of wake-up time duration of UE in consideration of the number of (re)transmission
    Battery Life is proportional to average user experience data rate
      Batter life is evaluated in consideration of RAN2 procedure