## Slide 1: Way Forward on LDPC Coding Schemes for NR
ZTE, ZTE Microelectronics, Nokia, Qualcomm, InterDigital, MediaTek, Intel, Samsung
3GPP TSG RAN WG1 #85 meeting
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.5.1
R1-165643

## Slide 2: Observations
    It is observed that Quasi-cyclic like LDPC codes are proposed and evaluated from companies considering LDPC, the Quasi-cyclic like LDPC codes include different names as follows:
    1) Quasi-cyclic LDPC codes
    2) Multiple-Edge LDPC codes
    3) Structured LDPC codes

## Slide 3: Proposal
    It is proposed that Quasi-cyclic like LDPC codes is defined as:
    The Parity check matrix of Quasi-cyclic like LDPC Codes is defined by a matrix H of size (mb×z)×(nb×z), which consists of sub-block matrices of size z×z, where each sub-block matrix is composed by circularly shifted matrices or zero matrices. Wherein, mb, nb and z are integers larger than 1.
    - The values of mb, nb and z are FFS.
    Multiple code rates and multiple code sizes should be supported. The granularity of information block size and code rate is FFS.
    How to support HARQ for LDPC is FFS.