## Slide 1: 3GPP TSG RAN WG1 Meeting #85 R1- 165645 Nanjing, China 23rd - 27th May 2016 Agenda item 6.1.6
WF on NPRACH UL gap
ZTE, MTK,Sony ……

## Slide 2: background
In the email discussions after RAN1 NB-IoT ad-hoc#2 meeting, the following was agreed:
Introduce uplink transmission gaps for long uplink (i.e. NB-PUSCH/NB-PRACH) transmissions.
The agreed CR for TS 36.211 implements this agreement with the following placeholder text:
Section 10.1.3.6:
In case of NPUSCH repetitions, after transmissions of [X] slots, a gap of [Y] slots shall be inserted where the NPUSCH transmission is postponed.
Similar to NPUSCH, NPRACH UL gap configuration scheme should be described in TS36.211. Method for selecting the starting subframe of RAR detecting window should also consider the case that NPRACH UL gap is inserted during NPRACH period.

## Slide 3: Proposals
Capture previous agreement in the CR: In the case of NPRACH repetition, after [X ms] transmission of NPRACH, a gap of [Y ms] shall be inserted.
If a NPRACH UL Gap is inserted at the end of NPRACH opportunity, the start of RAR detecting window is from the end of the UL gap.