## Slide 1: WF on SI messages for NB-IoT
ZTE, Nubia Technology, …
R1-165663
3GPP TSG RAN WG1 meeting #84bis
Nanjing, China, 23rd-27th May, 2016
Agenda item 6.1.6

## Slide 2: Background (1)
LS from RAN2 R1-165417 LS on TB sizes for SI-messages
  Propose using 56 bits and 120 bits as two additional TB sizes from the agreed TBS table for NPDSCH.
  RAN2 respectfully asks RAN1 to feedback early at RAN1#85 meeting whether adding two new TB sizes of 56 bits and 120 bits for SI messages is possible, and if so, to inform RAN2 which values of ITBS/ISF from TS 36.213 should be used.

## Slide 3: Background (2)
RAN1 NB-IoT adhoc#2 agreements:
  One transport block of an SI message is transmitted over 8 consecutive valid DL subframes.

## Slide 4: Proposal
An SI message with TBS equal to 56 bits and 120 bits is transmitted over 8 consecutive valid DL subframes.
  4 repetitions on top of
    ISF = 1, ITBS = 1 for 56 bits
    ISF = 1, ITBS = 4 for 120 bits