## Slide 1: Way forward on categorization of IFFT-based waveform candidates
Orange, Spreadtrum, InterDigital, ZTE, Cohere, Telstra, …
3GPP TSG RAN WG1 Meeting #85 R1-16xxxx
Nanjing, China, 23-27 May 2016
Agenda Item: 7.1.3.1

## Slide 2: Background
In RAN1-84b meeting, different IFFT-based waveform candidates have been presented, which can be divided into,
time domain windowing (TDW)
time domain filtering (TDF)
no windowing/filtering

## Slide 3: Background
The IFFT-based new waveform candidates presented in RAN1-84bis, include
W-OFDM (R1-162200, R1-163224)
FB-OFDM (R1-162225)
FBMC-OQAM (R1-162750)
f-OFDM (R1-162152)
FCP-OFDM (R1-162516)
UF-OFDM (R1-162890)
UW-DFT-s-OFDM (R1-162925, R1-164028)
ZT-s-OFDM (R1-162200)
GFDM (R1-165113)
OTFS (R1-163619)
More from RAN1-85, e.g.
FC-OFDM (R1-164619): a flavor of W-OFDM
GI DFT-s-OFDM (R1-164176)

## Slide 4: Proposal
Categorization of IFFT-based waveform candidates can be summarized as
* Application of time domain windowing or filtering to OTFS is FFS
 | time domain windowing | time domain filtering | w.o. windowing/filtering
multi-carrier (MC) | FBMC-OQAM FB-OFDM FC-OFDM GFDM W-OFDM OTFS* | f-OFDM FCP-OFDM UF-OFDM OTFS* | CP-OFDM OTFS
single-carrier (SC) | DFT spreading + TDW MC candidates | DFT spreading + TDF MC candidates | DFT-s-OFDM ZT-s-OFDM UW DFT-s-OFDM GI DFT-s-OFDM