## Slide 1: Way forward on timeline for sensing based UE autonomous resource selection
NTT DOCOMO, NEC, Samsung,…
R1-165698
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016
Agenda item 6.2.2.2.2

## Slide 2: Background
In RAN1#84bis, the following observation on sensing based resource selection is made:
If at TTI n resource selection/reselection is triggered in UE autonomous resource selection mode,
  The UE at least senses between TTI n-a and TTI n-b (FFS a and b with a>b>0), where a and b are integers
    Working assumption: The values a and b are common for V2V UEs.
  UE selects time-frequency resource(s) for PSSCH
  UE transmits SA in TTI n+c where c is an integer
    FFS whether c is a fixed value (>= 0) or variable.
In UE autonomous resource selection mode,
  UE transmits SA at TTI n+c indicating the associated data which is transmitted at TTI n+d (FFS d with d>=c), where c and d are integers
  UE indicates whether it intends to reuse the frequency resource signaled for transmission at TTI n+d for potential transmission at TTI n+e for another TB (FFS e with d<e), where e is an integer
    FFS whether this indication is implicit or explicit.
    FFS if and how to signal the value for e
    FFS how the UE determines the value for e
    FFS whether e is a single value or can be multiple values
    FFS whether, and if so how, a UE can notify later that it no longer intends to use the resource at TTI n+e.
    FFS how the UE decides to indicate this
    Other details FFS

## Slide 3: Proposal
The value of b is fixed
  b > 0
  Sensing window a-b has a single duration which is UE common
  The duration is equal to maximum supported interval for intention of next TB transmission, e.g., a-b = 1000 ms
  If UE skips sensing on sub-frame m, for e.g.: due to its own transmission in sub-frame m, it excludes resources in subframes at m+100*k, until it is able to perform sensing in those sub-frames.
c and d is selected by UE
  c > 0
  c, d <Ns
  At least Ns <= 100 is supported
  FFS: whether Ns is variable or not
Single value of e-d is derived from the information in SA.
It is FFS whether the value of e-d is explicitly signaled by SA or derived from the information in SA.
Sensing UE assumes that detected intentions for next TB transmission are repeated with inter-TB duration.
  FFS: values for e-d

## Slide 4: Example
(Re)selection
triggered
t
Sensing
n
n-a
n-b
n+c
n+d
SA
data
SA
data
Next TB transmission
n+e
n+Ns
Sensing window
Selection