## Slide 1: WF on SLS evaluation assumptions for eV2X
LG Electronics, Deutsche Telekom
3GPP TSG RAN WG1 Meeting #85 R1-165704
Nanjing, China, 23rd - 27th May 2016
Agenda item: 7.1.2

## Slide 2: Proposal
After email discussion, we proposed the modified SLS evaluation assumptions for eV2X.

## Slide 3: Proposal
SLS evaluation assumptions for eV2X
Parameters | Urban grid for eV2X | Highway for eV2X
Layout | Option 1: Macro only (with the road configuration in Figure 6.1.10-1 in TR38.913) Option 2: Macro + RSUs (with the road configuration in Figure 6.1.10-1 in TR38.913) Note: An RSU can be a BS type RSU or UE type RSU Out of coverage can be evaluated assuming eNB or RSU to be disabled. Sidelink evaluation with partly out of coverage Ues and partly in coverage Ues are FFS. | Option 1: Macro only (straigntline eNB placement with Road configuration in TR36.885) Option 2: Macro + RSUs (straightline eNB with Road configuration in TR36.885) Note: An RSU can be a BS type RSU or UE type RSU Out of coverage can be evaluated assuming eNB or RSU to be disabled. Sidelink evaluation with partly out of coverage Ues and partly in coverage Ues are FFS.
Inter-BS distance | Inter Macro: 500m Inter RSU: RSU is dropped at each intersection | Inter Macro: 500m or 1732m Inter RSU: Uniform allocation with 100m spacing in the middle of the highway

## Slide 4: Proposal
Carrier frequency | Macro to/from vehicle/pedestrian UE : 4 GHz Between vehicle/pedestrian UE: 4 GHz or 6 GHz BS-type-RSU to/from vehicle/pedestrian UE : 4 GHz UE-type-RSU to/from vehicle/pedestrian UE: 6 GHz | Macro to/from vehicle/pedestrian UE : 2 GHz or 4GHz Between vehicle/pedestrian UE: 4 GHz or 6 GHz BS-type-RSU to/from vehicle/pedestrian UE : 4 GHz UE-type-RSU to/from vehicle/pedestrian UE: 6 GHz
Aggregated system bandwidth | Up to 200 MHz (DL+UL) Up to 100 MHz (SL) | Up to 200 MHz (DL+UL) Up to 100 MHz (SL)
Simulation bandwidth | 20 or 40 MHz (DL+UL) 10 or 20 MHz (SL) | 20 or 40 MHz (DL+UL) 10 or 20 MHz (SL)
Channel model | Macro to/from vehicle/pedestrian UE : 2D UMa Between vehicle/pedestrian UE: V2X Channel model in TR36.885 RSU to/from vehicle/pedestrian UE : V2X Channel model in TR36.885 Note: Further study or 5GCM if needed, e.g. vertical beamforming, vehicle-to-vehicle channel | Macro to/from vehicle/pedestrian UE: 2D UMa for 500m ISD 2D RMa for 1732m ISD Between vehicle/pedestrian UE: V2X Channel model in TR36.885 RSU to/from vehicle/pedestrian UE : V2X Channel model in TR36.885 Note: Further study or 5GCM if needed, e.g. vertical beamforming, vehicle-to-vehicle channel

## Slide 5: Proposal
Tx power | Macro BS: 49dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 49dBm [TBD for TDD] BS-type-RSU: 24dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 24dBm Vehicle/pedestrian UE or UE type RSU: 23dBm Note: 33dBM for RSU or UE is not precluded | Macro BS: 49dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 49dBm [TBD for TDD] BS-type-RSU: 24dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 24dBm Vehicle/pedestrian UE or UE type RSU: 23dBm Note: 33dBM for RSU or UE is not precluded
BS antenna configuration | Macro BS: Up to 256 TX/RX antenna elements BS-type-RSU: Up to 8 TX/RX antenna elements | Macro BS: Up to 256 TX/RX antenna elements BS-type-RSU: Up to 8 TX/RX antenna elements
BS antenna pattern | Macro BS: Follow the modeling of TR 36.814 BS-type RSU: Follow the modeling of TR 36.814 Note: Further study if needed, e.g., vertical beamforming, vehicle-to-vehicle channel. | Macro BS: Follow the modeling of TR 36.814 BS-type RSU: Follow the modeling of TR 36.814 Note: Further study if needed, e.g., vertical beamforming effect, vehicle-to-vehicle channel.
BS antenna height | Macro BS: 25m BS-type-RSU: 5m | Macro BS: 35m for ISD 1732m 25m for ISD 500m BS-type-RSU: 5m
BS antenna element gain + connector loss | Macro BS: 8 dBi BS-type-RSU: 8dBi | Macro BS: 8 dBi BS-type-RSU: 8dBi
BS receiver noise figure | Macro BS:5dB BS-type-RSU: 5dB | Macro:5dB BS-type-RSU: 5dB

## Slide 6: Proposal
UE antenna elements | Vehicle/pedestrian UE: Up to 8 TX/RX antenna elements UE-type RSU: Up to 8 TX/RX antenna elements | Vehicle/pedestrian UE: Up to 8 TX/RX antenna elements. UE-type RSU: Up to 8 TX/RX antenna elements
UE antenna pattern | Vehicle/pedestrian UE: Half spherically uniform distribution with upper direction UE-type-RSU: Half spherically uniform distribution with bottom direction Note: directional antenna pattern is not precluded | Vehicle/pedestrian UE: Half spherically uniform distribution with upper direction UE-type-RSU: Half spherically uniform distribution with bottom direction Note: directional antenna pattern is not precluded
UE antenna height | Vehicle/pedestrian UE: 1.5m UE-type-RSU: 5 m | Vehicle/pedestrian UE: 1.5m UE-type-RSU: 5 m
UE antenna gain | Vehicle UE: 3dBi Pedestrian UE: 0dBi UE-type RSU: 3dBi | Vehicle UE: 3dBi Pedestrian UE: 0dBi UE-type RSU: 3dBi
UE receiver noise figure | Vehicle UE: 9dB UE-type RSU: 9dB | Vehicle UE: 9dB UE-type RSU: 9dB

## Slide 7: Proposal
Traffic model | [50 messages] per 1 second with [60km/h], [10 messages] per 1 second with [15km/h] in TR38.913 Note: This value is tentative. After SA1 input, it can be modified. | [50 messages] per 1 second with absolute average speed of [100-250 km/h] (relative speed: 200 – 500km/h) in TR38.913 Note: This value is tentative. After SA1 input, it can be modified.
Traffic load (Resource utilization) | FFS | FFS
UE distribution | Urban grid model (car lanes and pedestrian/bicycle sidewalks are placed around a road block. 2 lanes in each direction, 4 lanes in total, 1 sidewalk, one block size: 433m x 250m) in TR38.913 Average inter-vehicle distance (between two vehicles’ center) in the same lane is [1sec * average vehicle speed ] (average speed [15 – 120km/h]) in TR38.913 Vehicle UE location update in TR36.885 should be used for the evaluation of PRR in sidelink or communication interruption in uplink/downlink. Vehicle UE location update may not be assumed for the evaluation of PRR in uplink/downlink Note: Inter-vehicle distance is tentative. After SA1 input, it can be modified. | Average inter-vehicle distance (between two vehicles’ center) in the same lane is [0.5 sec, 1sec * average vehicle speed] (average speed: [100-250 km/h]) in TR38.913 Vehicle UE location update in TR36.885 should be used for the evaluation of PRR in sidelink or communication interruption in uplink/downlink. Vehicle UE location update may not be assumed for the evaluation of PRR in uplink/downlink Note: Inter-vehicle distance is tentative. After SA1 input, it can be modified.

## Slide 8: Proposal
UE receiver | MMSE-IRC as the baseline receiver Note: Advanced receiver is not precluded. | MMSE-IRC as the baseline receiver Note: Advanced receiver is not precluded.
Feedback assumption | FFS | FFS
Channel estimation | Realistic | Realistic
Performance metric | FFS | FFS