## Slide 1: Way forward on processing timing reduction for sTTI
Ericsson
R1-165707
AI 6.2.10.2
3GPP RAN WG 1 #85
23rd – 27th May2016, Nanjing , P.R. China

## Slide 2: Background
The system evaluation provided to RAN1 #85 shows that
  if the processing time cannot be linearly scaled with TTI length but remains close to the linearly scaled value, short TTI significantly improves data rate
  subframe long TTI with reduced processing time can improve user performance
Maximum TA affects the minimum delay between UL grant reception and UL data transmission and between the DL data reception and DL HARQ feedback transmission

## Slide 3: Proposal (1)
It is recommended to limit the maximum TA for short TTI operation

## Slide 4: Proposal (2)
The following options are considered for DL and UL processing time reduction for short TTI operation.
  The minimum delay between UL grant and UL data and between DL data and DL HARQ feedback is 4 + k sTTI
    Option 1:
      k = 0
    Option 2:
      k is fixed for a given sTTI length with 0 <= k <= 4
      Example values are
        k = 4 sTTI in case of 2 os TTI
        k = 2 sTTI in case of 4 os TTI
        k = 1 sTTI in case of slot based TTI
    Option 3:
      k is indicated by eNB, where k is selected from a pre-defined set and k<= 4
        Example of pre-defined set: {0, 1, 2, 4}, {-1, 0, 1, 2}, …
        The value selected for k may depend on sTTI length and/or UE capability and/or TA
        FFS: semi-static or dynamic configuration of k
    Option 4
      k < 0 for slot based TTI. Examples: k = -2, k= -1
      FFS value of k for 2os and 4 os TTI
    Note that sTTI refers to
      sPUSCH sTTI for the UL grant to UL data timing
      sPDSCH sTTI for the DL data to DL HARQ feedback timing

## Slide 5: Proposal (3)
The following options are considered for DL and UL processing time reduction for subframe-long TTI operation for short TTI capable UEs
  The minimum delay between UL grant and UL data, and between DL data and DL HARQ feedback is k subframes
    Option1:
      k = 2
    Option 2:
      k = 3
    Option 3:
      k = 4
    FFS potential TBS restriction
  The timing from DL data to some CQI feedback is n + k TTI, k is FFS