## Slide 1: WF on CW adjustment for UL LBT based on Cat. 4
Ericsson, [Huawei, HiSilicon], [Nokia]….
3GPP TSG RAN WG1 #85 R1-165713
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.5
Document for decision

## Slide 2: Background
DL |  | DL |  | UL H0 N1 | UL H1 N1 | DL | UL H2 N1 | UL H3 N1 | DL | UL H4 N1 | UL H5 N1 | DL | UL H0 N0 | UL H1 N1 | DL |  | UL H2 N1 | UL H3 N1 |  | UL H4 N1 | UL H5 N0
No UL TX due to LBT failure
UL not received at eNB
UL not received at eNB
UL
Hx
Ny
Hx: HARQ process x
Ny: NDI of HARQ process X equal to y
Where y=0 or 1
Reference HARQ process in the yellow subframe

## Slide 3: Proposal
The CWS is adjusted for all the LBT priority classes used by the UE.
The UE shall follow the procedure below to increase or reset to the CWS for performing a Cat. 4 LBT prior to transmission of a UL burst
  The most recent scheduled burst of contiguous subframes (excluding the currently scheduled burst) for which HARQ process number used in the first transmitted subframe of that burst also appears in the currently scheduled burst is used as the reference transmission burst by the UE. The HARQ process which satisfies the above condition is used as the reference HARQ process to determine the contention window size.
  If the NDI bit for the reference HARQ process is not toggled in TM1, or if the NDI bits for both TBs for the reference HARQ process are not toggled in TM2 the NDI bit for the reference HARQ process is set to 0, the CWS is increased to the next higher value in the set of CWSs for the priority class that was used to perform LBT prior to transmission of the reference transmission burst.
  Otherwise if the NDI bit for the reference HARQ process is set to 1, the CWS is reset to the minimum value in the set of CWSs for the priority class that is being used by the UE to perform LBT prior to transmission of the current transmission burst.

## Slide 4: Proposal (cont)
  The CW size is reset to the minimum value if the maximum CW size is used for K consecutive LBT attempts for transmission
      K is selected by implementation from the set of values from (1, …,8).