## Slide 1: WF on PUSCH Transmissions with 25 µs CCA Period
Ericsson, …
3GPP TSG RAN WG1 #85 R1-165717
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.5
Document for decision

## Slide 2: Background
Multiple agreements refer to a 25 µs CCA immediately prior to transmission on the UL
We also have following agreement which indicates FFS on starting PUSCH within DFTS-OFDM symbol 0
Agreements:
Dynamic signaling indicates whether PUSCH in a UL subframe is transmitted from
  Start of DFTS-OFDM symbol 0 or
  Start of DFTS-OFDM symbol 1
  FFS: Within DFTS-OFDM symbol 0
Dynamic signaling indicates whether PUSCH in a UL subframe is transmitted up to OFDM symbol 13 or OFDM symbol 12
Any combination of above options can be enabled by the dynamic signaling

## Slide 3: Background
For the first UL subframe from a UE that follows a full DL or UL subframe, the 25 µs LBT needs to be performed within DFTS-OFDM symbol 0
It is important for LAA to be able to share the channel occupancy with gap of no more than 25 µs
It is desirable for the 25 µs LBT to be at the beginning of the subframe followed by the UL transmission

## Slide 4: Background
Simply puncturing modulation symbols from existing LTE PUSCH signal results in substantial losses in link performance and throughput. The losses are higher for MCSs with higher coding rates. In some cases, unexpectedly higher losses can happen in certain combinations

## Slide 5: Background
We consider three cases:
Baseline case (Case #3 in Figure): no muting of samples on any SC-FDMA symbol
Worst muting case (Case #2 in Figure): muting the first 25 μs of the first SC-FDMA symbol of every UL subframe. This is the worst case muting scenarios for LAA UL operations.
Unrealistic boundary case (Case #1 in Figure): muting the first 25 μs of every SC-FDMA symbol. This is a boundary case for comparison and is not according to LAA UL operations.
Muting the first 25 μs of the first SC-FDMA symbol, even if it is done for every UL subframe, does not cause meaningful increase in out-of-band emission.

## Slide 6: Proposal
PUSCH is transmitted by rate matching around the modulation symbols corresponding to the first 25 µs of DFTS-OFDM symbol 0 and also around the modulation symbols at the end of DFTS-OFDM symbol 0 corresponding to the cyclic prefix length