## Slide 1
Discussion on frequency-domain initiated numerology and time-domain initiated numerology
CMCC
3GPP TSG-RAN WG1 #85 R1-165719
23th – 27th May 2016
Nanjing, China
Agenda item: 7.1.4

## Slide 2
Scale factors N =2n for subcarrier spacing on top of assumed basic subcarrier spacing 15KHz
Frequency domain initiated numerology-observation 1
Possible design guided by this numerology assumption
  Option 1: Same CP overhead regardless of numerologies
  Option 2: Comparable CP length regardless of numerology
Option 1 | 15KHz | 30KHz | 60KHz
Symbol duration | 66.67 | 33.33 | 16.67
CP length | 4.76 | 2.38 | 1.19
Number of OS in 1ms duration | 14 | 28 | 56
Overhead of CP | 7% | 7% | 7%
Option 2 | 15KHz | 30KHz | 60KHz
Symbol duration | 66.67 | 33.33 | 16.67
CP length | 4.76 | 5.12 | 4.17
Number of OS in 1ms duration | 14 | 26 | 48
Overhead of CP | 7% | 13.4% | 20%

## Slide 3
Scale factors N =2n for number of OS on top of assumed spacing 17.5KHz
Time domain initiated numerology-observation 1
Possible design guided by this numerology assumption
  Option 1: Same CP overhead regardless of numerologies
  Option 2: Comparable CP length regardless of numerology
Option 1 | 17.5KHz | 35KHz | 70KHz
Symbol duration | 57.14 | 33.33 | 16.67
CP length | 5.36 | 2.68 | 1.34
Number of OS in 1ms duration | 16 | 32 | 64
Overhead of CP | 8.6% | 8.6% | 8.6%
Option 2 | 17.5KHz | 37.5KHz | 90KHz
Symbol duration | 57.14 | 26.67 | 11.11
CP length | 5.36 | 4.58 | 4.52
Number of OS in 1ms duration | 16 | 32 | 64
Overhead of CP | 7% | 14.7% | 28.9%

## Slide 4
4
NB-IOT has to sample at 1.92 MHz due to LTE un-even symbol duration
NR mMTC mode have much lower sampling rate and FFT complexity
Time/frequency domain initiated numerology-observation 2

## Slide 5
Two different approaches to achieve shorter TTIs
  Scaling subcarrier spacing by 2^K: better pipeline processing
  Scaling the number of symbols per TTI by 1/2^K: Robustness
TTI multiplexing is inefficient in LTE due to 7-symbol numerology
  Symbol scaling does not work, lead to half symbol
Time/frequency domain initiated numerology-observation 3

## Slide 6
Questions for future design
The motivation of induction of scaled numerologies just for critical use cases where spectrum efficiency is less important?
  Is it also for latency?
CP length will not be guaranteed even different numerologies multiplexed in single “carrier” where same propagation model/delay spread is same for all numerologies?
  CP length can be scaled down regardless actual delay spread/ISI for some numerologies
Are there any conclusion/gap analysis on the guardband required for 2^m SCS and 2^m OS when considering different numerologies multiplexed

## Slide 7
Proposals
RAN1 should carefully make decision on such kind of key parameters and design principle than dependent on more studies and evaluation. Especially full comparison from different aspects should be done to guarantee we are on the right way. Based on above observation. we propose to do some comparison from following aspects(not limited to):
  Design complexity and future design effort
  Overall performance
  Compatibility of different numerology from time domain and frequency domain
  Multiplexing efficiency
  Latency
  Coexistence with NB-IoT and LTE
  Scalable set of supportable CC BW