## Slide 1: WF on HARQ feedback for DL broadcast
LG Electronics, Huawei, ITRI
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd – 27th May 2016
Agenda item: 6.2.9.2.1
R1-165729

## Slide 2: Proposal
Two options are identified in resource allocation for HARQ feedback for DL multicast/broadcast transmissions:
  UE-common resource: Multiple UEs receiving the same DL multicast/broadcast transmission transmit HARQ feedback on the same resource.
  UE-specific resource: Different UEs receiving the same DL multicast/broadcast transmission transmit HARQ feedback on different resources.
Comparison between the two options in the next slide is captured in the TR.
Network can perform a slow MCS adaptation or multicast/broadcast retransmissions based on HARQ feedback for DL multicast/broadcast transmissions.

## Slide 3: Proposal
 | Pros | Cons
UE-common resource | - Overhead for HARQ-ACK can be reduced. | - Interference to other UL channel may be high and uncontrollable. - It may be difficult to be multiplexed with other UL transmission. - It may be difficult for eNB to recognize scheduling message miss in a UE. - eNB can hardly recognize the position of UEs that fail reception
UE-specific resource | - Multiplexing with unicast UL can be easy. - Multiplexing multiple HARQ-ACK for DL multicast/broadcast can be easy. - UE’s missing the scheduling message can be detected in the eNB. | - Overhead for HARQ-ACK can be high.