## Slide 1: Way forward on V2V Tx gap
NTT DOCOMO, LG Electronics
R1-165733
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016
Agenda item 6.2.2.6.1

## Slide 2: Background
In RAN1#84bis, the following agreement on coexistence of PC5-based V2V operation and legacy Uu operation is made:
The followings are supported for the purpose of coexistence between PC5-based V2V and WAN:
  Sidelink open loop power control is re-used for SL TX for V2V
    FFS RSRP based resource selection
  SL TX for V2V can be prioritized over WAN TX
    FFS the details (e.g., applicability to Mode 1 and/or Mode 2, etc.), especially whether existing D2D mechanism can be reused,
    The prioritization is managable by eNB. Details FFS.
  The same receiver capability of D2D communication UEs is assumed for V2V UEs. That is, a Rx chain is available at all time to receive V2V signals without affecting WAN reception (from RAN1 perspective) when the UE is configured to receive V2V.

## Slide 3: Proposal
Rel-13 SL TX gap is extended for prioritization of SL V2V Tx over WAN UL Tx.
  Gap pattern needs to be optimized to cover SL V2V Tx.
    Details are up to RAN2.
As Rel-13 SL Tx gap, UE can only prioritize SL V2V Tx over WAN UL Tx during configured Tx gap.
  If UE is not configured with Tx gap, the UE prioritizes WAN UL Tx over SL V2V Tx.
In UE autonomous resource selection, UE resource selection is not affected by the configuration of SL TX gap