## Slide 1
3GPP TSG RAN WG1 Meeting #85bis R1-165735
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2
Way forward on assumption details for Case 5 in waveform LLS evaluation
Spreadtrum, Fraunhofer IIS, National Taiwan University, Orange, ZTE

## Slide 2: Background
Proposed:
  Case 5: UL asynchronous reception with possible in-band interference, under the assumption that each target UE is moving in the cell
    Case 5a: A single target UE with asynchronous reception.
    Case 5b: Multiple target co-channel UEs with respective time offsets

## Slide 3: TA calibration for relaxed synchronization with sporadic UL transmissions in mMTC

## Slide 4: Scenario illustration for 1 UE

## Slide 5: Time offset with TA Calibration
  Receiver time offset =
  The range of is

## Slide 6: Parameter values for each UE (1/2)
1 min
km/h
  The range of UL time offset: [- 1.6 us, 1.6 us]

## Slide 7: Parameter values for each UE (2/2)
  Time-offset generation modes (TGM):
  TGM 1: Worst and best cases
    3 UL time offset samples: -1.6 us, 0, 1.6 us
  TGM 2: Random generation
    Generate samples independently per drop
    10, 000 independent drops, 1 subframe/drop

## Slide 8: More parameters for 2 UEs
2 UEs:
  2 Rx antennas at the receiver, 1 Tx antenna at each UE
  MIMO receiver: LMMSE
  Far UE: UE 0. Near UE: UE 1.
  Receiver power offsets between UEs: 0 dB, 10 dB, 20 dB, UE 0’ s power is not greater than UE 1’s
  UL time offset sets: UE 0’s time offset is not smaller than UE1’s

## Slide 9: Parameters for Case 5
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD /TDD
Subframe duration | 1 ms as baseline, other duration is FFS (short duration could be considered)
Subcarrier spacing | 15KHz as baseline
Guard time interval | 4.7us as baseline, other interval is FFS
FFT size | 1024 for 15KHz subcarrier spacing
Bandwidth per user | 720 KHz (48 Subcarriers allocated per user)
Number of uplink users | Case 5a: 1 UE Case 5b: 2 UEs
Power offset in case 5b | 0 dB, 10 dB, 20 dB
Antenna configuration | 1T, 2R
MIMO receiver | LMMSE
MCS | Fixed. QPSK: 1/2
Control overhead | Zero
Time offset of each UE | TGM 1: Worst and best cases TGM 2: Random generation
Channel estimation * | Ideal
Channel model | TDL model All values of DS {10, 30, 100, 300, 1000} ns are evaluated with the selected TDL-DS combinations, i.e. TDL-A for DS {10,30}ns, TDL-B for DS {100 }ns, TDL-C for DS {300,1000}ns. Companies are allowed to choose additional combination(s) of other DS values and TDL–A and/or TDL-C in TR38.900. ETU/EPA/EVA are optional. Mobility: 30 km/h