## Slide 1: WF on semi-persistent transmission for mode 2
Ericsson, Qualcomm
3GPP TSG RAN WG1 Meeting #85 R1-165740
Nanjing, China, 23rd - 27th May 2016
Agenda item: 6.2.2.2

## Slide 2: Proposal
  A UE indicates that it intends to reuse (for potential transmission) the frequency resource signaled for transmission in the SA with a period of 100ms
    e = d + k*100 ms (k=1,2,…)
    FFS terminating conditions (e.g., timeout, explicit release, underutilization, etc.)
    (a-b) is 1 second
      SA signaling resource(s) at any TTI (n-a,n-b) are taken into account even if they are transmitted earlier than TTI n-a
  UE signals in SA the predicted time of its next transmission (e.g., k=3 for transmission in 300 ms)
    Maximum value of k = 10
    Time for next transmission prediction is specified as a function of arrival time of previous packets
      Details FFS
    Receiver UE uses this information
      The eNB/pre-configuration may configure UEs to ignore this information
      FFS other details