## Slide 1: WF on NB-IoT Multi-PRB operation
LG Electronics, Nokia, ASB
3GPP TSG RAN WG1 Meeting #85 R1-165747
Nanjing, China, 23th – 27th May 2016
Agenda Item: 6.1.6

## Slide 2: Proposal
When a UE is configured with additional PRB in inband where anchor PRB is in guard band
    If same-PCI indicator is true,
      Assume that cell ID from anchor carrier is used for legacy CRS in the additional PRB
      The same number of antenna ports used in NB-RS in the anchor carrier is used for legacy CRS transmission
    If same-PCI indicator is not true
      Vshift value of legacy CRS is implicitly derived (i.e., the same Vshift between NB-RS and legacy CRS is assumed)