## Slide 1: Way Forward on MUST Power Ratio Set
Qualcomm, …
R1-165763
3GPP TSG-RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 6.2.4.1

## Slide 2: Background
The number of power ratios is mostly a fairness, MUST gain and complexity tradeoff
  We don’t believe the extra MUST gain is substantial enough to worth the extra complexity though
The power ratio selection greatly affects the receiver complexity and chip area
  If multiple power ratios is absolute necessary, the selection should consider implementation complexity
  The set of numbers in the proposal is assuming a underlying uniform extended constellation

## Slide 3: Proposals
The power ratio is down selected from the next table as a function of near and far UE modulation order
  The highlighted entries corresponds to uniform combined constellation and are mandatory
  The other entries in each row, if selected, are UE capability and are optional
MODN+MODF |  |  |  |  |  |  | 
QPSK+QPSK | 9/13 (0.692) | 4/5 (0.8) | 25/29 (0.862) | 16/17 (0.941) | 36/37 (0.973) |  | 
16QAM+16QAM | 49/69 (0.71) | 16/21 (0.762) | 81/101 (0.802) | 36/41 (0.878) | 64/69 (0.928) | 100/105 (0.952) | 144/149 (0.966)
QPSK+64QAM | 100/121 (0.826) |  |  |  |  |  | 
16QAM+QPSK | 80/89 (0.8989) | 20/21 (0.9524) | 80/81 (0.9879) |  |  |  | 
16QAM+16QAM | 80/85 (0.9412) |  |  |  |  |  |