## Slide 1
Way Forward for RMa model frequency range
Telstra, Ericsson
R1-165769
replacing R1-164975

## Slide 2: Background
Measurements were collected at 24 GHz in a rural macro environment and were found to agree with the existing RMa macro (R1-164975)
Based on this measurement campaign, the applicability of the pathloss model can be extended to 30 GHz
It was requested that the limitations of the measurement campaign be recorded

## Slide 3: Way forward proposal
Proposal: Extend the applicability of the RMa model to 30 GHz for pathloss, noting that:
All fast fading aspects remain applicable to 7 GHz
Pathloss model validation above 7 GHz is based on a single measurement campaign conducted at 24 GHz
  This sentence will be captured as a footnote to the pathloss table in the TR