## Slide 1: WF on handling PUSCH errors after 25us LBT in eLAA
Broadcom,..
3GPP TSG RAN WG1 #85 R1-16xxxx
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.1
Document for decision

## Slide 2: Proposal
Errors detected in UL transmissions occurring immediately after 25us LBT within a Channel Occupancy obtained by the eNB based on CAT4 LBT, shall be handled as follows:
  Option 1: eNB abandons the current COT i.e. does not send any more DL transmissions or UL grants
  Option 2: The UL CWS of the corresponding UE is doubled (will be indicated and used only the next time CAT4 LBT is signaled to the UE)
  Option 3: The next time the UE is given a UL grant, it is always with a CAT4 LBT
  Option 4: Combinations of the above